## Slide 1: Simplified Critical-State Soil Mechanics
Paul W. Mayne
Georgia Institute of Technology
08 July 2014

## Slide 2: PROLOGUE
Critical-state soil mechanics is an effective stress framework describing mechanical soil response
In its simple form here, we consider only shear loading and compression-swelling.
We merely tie together two well-known concepts: (1) one-dimensional consolidation behavior (via e-logsv’ curves); and (2) shear stress-vs. normal stress (t-sv’) plots from direct shear (alias Mohr’s circles).

## Slide 3: Critical State Soil Mechanics (CSSM)
Experimental evidence
  1936 by Hvorslev (1960, ASCE)
  Henkel (1960, ASCE Boulder)
  Parry (1961)
  Kulhawy & Mayne (1990): Summary of 200+ soils
Mathematics presented elsewhere
  Schofield & Wroth (1968)
  Roscoe & Burland (1968)
  Wood (1990)
  Jefferies & Been (2006)
Basic form: 3 material constants (f', Cc, Cs) plus initial state parameter (e0, svo', OCR)

## Slide 4: Critical State Soil Mechanics (CSSM)
Constitutive Models in FEM packages:
  Original Cam-Clay (1968)
  Modified Cam Clay (1969)
  NorSand (Jefferies 1993)
  Bounding Surface (Dafalias)
  MIT-E3 (Whittle, 1993)
  MIT-S1 (Pestana, 1999; 2001)
  Cap Model
  “Ber-Klay” (Univ. California)
  others (Adachi, Oka, Ohta, Dafalias, Nova, Wood, Huerkel)
"Undrained" is just one specific stress path
Yet !!! CSSM is missing from most textbooks and undergrad & grad curricula.

## Slide 5: One-Dimensional Consolidation
Cc = 0.38
Cr = 0.04
svo'=300 kPa
sp'=900 kPa
Overconsolidation Ratio, OCR = 3
Cs = swelling index (= Cr)
cv = coef. of consolidation
D' = constrained modulus
Cae = coef. secondary compression
k ≈ hydraulic conductivity
sv’

## Slide 6
Direct Shear Test Results
sv’
t
Direct Shear Box (DSB)
sv’
t
Direct Simple Shear (DSS)
t
d
t
gs

## Slide 7: CSSM for Dummies
sCSL’ sNC’
Effective stress sv'
Shear stress t
Void Ratio, e
NC
CC
tanf'
CSL
Effective stress sv'
Void Ratio, e
NC
CSL
CSSM Premise:
“All stress paths fail on the critical state line (CSL)”
CSL
f
c=0
e0
sCSL’  ½sNC’
Log sv'

## Slide 8: CSSM for Dummies
Log sv'
Effective stress sv'
Shear stress t
Void Ratio, e
Void Ratio, e
NC
NC
CC
tanf'
CSL
CSL
CSL
STRESS PATH No.1
NC Drained Soil
Given: e0, svo’, NC (OCR=1)
e0
svo
svo
Drained Path: Du = 0
tmax = c + s tanf
ef
De
Volume Change is Contractive: evol = De/(1+e0) < 0
Effective stress sv'
c’=0

## Slide 9: CSSM for Dummies
Log sv'
Effective stress sv'
Shear stress t
Void Ratio, e
Void Ratio, e
NC
NC
CC
tanf'
CSL
CSL
CSL
STRESS PATH No.2
NC Undrained Soil
Given: e0, svo’, NC (OCR=1)
e0
svo
svo
Undrained Path: DV/V0 = 0
+Du = Positive Excess Porewater Pressures
svf
svf
Du
tmax = cu=su
Effective stress sv'

## Slide 10: CSSM for Dummies
Log sv'
Effective stress sv'
Shear stress t
Void Ratio, e
NC
NC
CC
tanf'
CSL
CSL
CSL
Note: All NC undrained
stress paths are parallel
to each other, thus:
su/svo’ = constant
Effective stress sv'
DSS: su/svo’NC = ½sinf’
Void Ratio, e

## Slide 11: CSSM for Dummies
Log sv'
Effective stress sv'
Effective stress sv'
Shear stress t
Void Ratio, e
Void Ratio, e
NC
NC
CC
tanf'
CSL
CSL
CSL
CS
sp'
sp'
OC
Overconsolidated States:
e0, svo’, and OCR = sp’/svo’
where sp’ = svmax’ = Pc’ =
preconsolidation stress;
OCR = overconsolidation ratio

## Slide 12: CSSM for Dummies
Log sv'
Effective stress sv'
Shear stress t
Void Ratio, e
NC
NC
CC
tanf'
CSL
CSL
CSL
CS
OC
Stress Path No. 3
Undrained OC Soil:
e0, svo’, and OCR
svo'
e0
svo'
Stress Path: DV/V0 = 0
Negative Excess Du
Effective stress sv'
svf'
Void Ratio, e
Du

## Slide 13: CSSM for Dummies
Log sv'
Effective stress sv'
Shear stress t
Void Ratio, e
Void Ratio, e
NC
NC
CC
tanf'
CSL
CSL
CSL
CS
OC
Stress Path No. 4
Drained OC Soil:
e0, svo’, and OCR
Stress Path: Du = 0
Dilatancy: DV/V0 > 0
svo'
e0
svo'
Effective stress sv'

## Slide 14: Critical state soil mechanics
Initial state: e0, svo’, and OCR = sp’/svo’
Soil constants: f’, Cc, and Cs (L = 1-Cs/Cc)
For NC soil (OCR =1):
  Undrained (evol = 0): +Du and tmax = su = cu
  Drained (Du = 0) and contractive (decrease evol)
For OC soil:
  Undrained (evol = 0): -Du and tmax = su = cu
  Drained (Du = 0) and dilative (Increase evol)
There’s more !
Semi-drained, Partly undrained, Cyclic response…..

## Slide 15: Equivalent Stress Concept
Log sv'
Stress sv'
Shear stress t
Void Ratio, e
NC
NC
CC
tanf'
CSL
CSL
CSL
CS
OC
1. OC State (eo, svo’, sp’)
svo'
2. Project OC state to NC line for equivalent stress, se’
3. se’ = svo’ OCR[1-Cs/Cc]
svo'
e0
Effective stress sv'
Void Ratio, e
sp'
sp'
se'
se'
su
svf'
ep
De = Cs log(sp’/svo’)
De = Cc log(se’/sp’)
De
at se’
suOC = suNC

## Slide 16: Critical state soil mechanics
Previously: su/svo’ = constant for NC soil
On the virgin compression line: svo’ = se’
Thus: su/se’ = constant for all soil (NC & OC)
For simple shear: su/se’ = ½sin f’
Equivalent stress:
Normalized Undrained Shear Strength:
su/svo’ = ½ sinf’ OCRL
where L = (1-Cs/Cc)
se’ = svo’ OCR[1-Cs/Cc]

## Slide 17: Undrained Shear Strength from CSSM

## Slide 18: Undrained Shear Strength from CSSM

## Slide 19: Porewater Pressure Response from CSSM

## Slide 20: Yield Surfaces
Log sv'
Normal stress sv'
Shear stress t
Void Ratio, e
NC
NC
CSL
CSL
CSL
OC
Normal stress sv'
Void Ratio, e
sp'
sp'
OC
Yield surface represents 3-d preconsolidation
Quasi-elastic behavior within the yield surface
Yield Surface

## Slide 21: Critical state soil mechanics
This powerpoint: geosystems.ce.gatech.edu
Classic book: Critical -State Soil Mechanics by Schofield & Wroth (1968): http://www.geotechnique.info
Schofield (2005) Disturbed Soil Properties and Geotechnical Design Thomas Telford
Wood (1990): Soil Behaviour and CSSM
Jefferies & Been (2006): Soil liquefaction: a critical-state approach www.informaworld.com

## Slide 22: ESA versus TSA
Effective stress analysis (ESA) rules:
  c' = effective cohesion intercept (c' = 0 for OCR < 2 and c' ≈ 0.02 sp' for short term loading)
  f' = effective stress friction angle
  t = c' + s' tan f' = Mohr-Coulomb strength criterion
  sv' = sv - u0 - Du = effective stress
Total stress analysis (TSA) is (overly) simplistic for clay with strength represented by a single parameter, i.e. "f = 0" and tmax = c = cu = su = undrained shear strength (implying "Du = 0")

## Slide 23: Explaining the myth that "f = 0"
The effective friction angle (f') is usually between 20 to 45 degrees for most soils. However, for clays, we here of "f = 0" analysis which applies to total stress analysis (TSA). In TSA, there is no knowledge of porewater pressures (PWP). Thus, by ignoring PWP (i.e., Du = 0), there is an illusional effect that can be explained by CSSM. See the following slides.

## Slide 24
(Undrained) Total Stress Analysis - Consolidated
Undrained Triaxial Tests
Three specimens initially consolidated
to svc' = 100, 200, and 400 kPa

## Slide 25: (Undrained) Total Stress Analysis
Chart: Effective stress, sv' (kPa)
TSP NC | 1 | 1
su100
su200
su400
In TSA, however, Du not known, so plot stress paths for "Du = 0"
Obtains the illusion that " f ≈ 0° "

## Slide 26
Another set of undrained Total Stress Analyses (TSA) for UU tests on clays:
UU = Unconsolidated Undrained

## Slide 27: (Undrained) Total Stress Analysis
Chart: Effective stress, sv' (kPa)
TSP NC | 1 | 1
su
Again, Du not known in TSA, so plot for stress paths for "Du = 0"
Obtains the illusion that " f = 0° "

## Slide 28: Explaining the myth that "f = 0"
Effective Stress Analyses (ESA)
  Drained Loading (Du = 0)
  Undrained Loading (DV/V0 = 0)
Total Stress Analyses (TSA)
  Drained Loading (Du = 0)
  Undrained Loading with "f = 0" analysis: DV/V0 = 0 and "Du = 0"

## Slide 29: Cambridge University q-p' space
P' = (s1' + s2' + s3')/3
q = (s1 - s3)
Triaxial
Compression
CSL
s2' = s3'
s1'
Undrained NC
Stress Path
Undrained OC
Stress Path
svo' = P0'
Drained
Stress Path
3V : 1H

## Slide 30: Port of Anchorage, Alaska

## Slide 31: Cavity Expansion – Critical State Model for Evaluating OCR in Clays from Piezocone Tests
where M = 6 sinf’/(3-sinf’)
and L = 1 – Cs/Cc  0.8
qc
fs
ub
 qT

## Slide 32: Cambridge University q-p' space
P' = (s1' + s2' + s3')/3
q = (s1 - s3)
CSL
Yield Surface
Original Cam Clay
Modified Cam Clay
Pc'
Bounding Surface
Cap Model

## Slide 33: Anisotropic Yield Surface
P’ = (s1’ + s2’ + s3’)/3
q = (s1 - s3)
Mc = 6sinf’/(3-sinf’)
fctn(K0NC)
Y3 = Limit State
Yield Surface
e0
svo’
K0
G0
Y2
CSL
sp’
Y1
OC
NC

## Slide 34: Cambridge University q-p' space
P' = (s1' + s2' + s3')/3
q = (s1 - s3)
fctn(K0NC)
Y3 = Limit State
Yield Surface
CSL
sp’
Ko Unloading
Apparent
Mc

## Slide 35: MIT q-p' space
P' = ½(s1' + s3')
q = ½(s1 - s3)
fctn(K0NC)
Yield Surface
sp’
OC
Natural Clays
Diaz-Rodriguez, Leroueil,
and Aleman (1992, JGE)

## Slide 36: Diaz-Rodriguez, Leroueil, & Aleman (ASCE Journal Geotechnical Engineering July 1992)
Yield Surfaces of Natural Clays

## Slide 37: Friction Angle of Clean Quartz Sands
(Bolton, 1986 Geotechnique)

## Slide 38: State Parameter for Sands, y (Been & Jefferies, 1985; Jefferies & Been 2006)
log p'
void
ratio
e
p' = ⅓ (s1'+s2'+s3')
VCL
CSL
l10
l10
p0'
y = e0 - ecsl
Dry of Critical (Dilative)
Wet of Critical
(Contractive)
e0
ecsl

## Slide 39: State Parameter for Sands, y (Simplified Critical State Soil Mechanics)
log p'
void
ratio
e
p' = ⅓ (s1'+s2'+s3')
VCL
CSL
l10
l10
p0'
y = e0 - ecsl
y = (Cs - Cc )∙log[ ½ cos f' OCR ]
Du = (1 - ½ cos f' OCRL ]∙svo'
e0
ecsl
then CSL = OCR = 2/cosf'

## Slide 40: State Parameter for Sands, y (Been, Crooks, & Jefferies, 1988)
log OCRp = log2L + Y/(k-l)
where OCRp = R = overconsolidation ratio in Cambridge q-p' space, L = 1-k/l, l = Cc/ln(10) = compression index, and k  Cs/ln(10) = swelling index

## Slide 41: MIT Constitutive Models
Whittle et al. 1994: JGE Vol. 120 (1) "Model prediction of anisotropic behavior of Boston Blue Clay"
MIT-E3: 15 parameters for clay
Pestana & Whittle (1999) "Formulation of unified constitutive model for clays and sands" Intl. J. for Analytical & Numerical Methods in Geomechanics, Vol. 23
MIT S1: 13 parameters for clay
MIT S1: 14 parameters for sand

## Slide 42: MIT E-3 Constitutive Model
Whittle (2005)

## Slide 43: MIT S-1 Constitutive Model
Pestana and Whittle (1999)

## Slide 44: MIT S-1 Constitutive Model
Predictions for
Berlin Sands
(Whittle, 2005)

## Slide 45: Critical state soil mechanics
Initial state: e0, svo’, and OCR = sp’/svo’
Soil constants: f’, Cc, and Cs
Link between Consolidation and Shear Tests
CSSM addresses:
  NC and OC behavior
  Undrained vs. Drained (and other paths)
  Positive vs. negative porewater pressures
  Volume changes (contractive vs. dilative)
  su/svo’ = ½ sinf’ OCRL where L = 1-Cs/Cc
Yield surface represents 3-d preconsolidation
State parameter: y = e0 - ecsl

## Slide 46: Simplified Critical State Soil Mechanics
Log sv'
Effective stress sv'
Effective stress sv'
Shear stress t
Void Ratio, e
Void Ratio, e
NC
NC
CC
CSL
CSL
CSL
CS
sp'
sp'
OC
Four Basic Stress Paths:
1. Drained NC (decrease DV/Vo)
2. Undrained NC (positive Du)
3. Undrained OC (negative Du)
4. Drained OC (increase DV/Vo)
f'
eNC
consolidation
swelling
eOC
1
2
3
4
Yield
Surface
dilative
contractive
+Du
-Du
sCS½sp
tmax = su NC
tmax = stanf
su OC
tmax = c+stanf
c'