## Slide 1: Seismic Piezocone Testing: The Versatile Means for Geotechnical Site Exploration in 2020 and Beyond
Paul W. Mayne, PhD, P.E., BS'74, ME'77, PhD'91
Georgia Institute of Technology
Tuesday 05 November 2019
366 Hollister Hall
21st Robert L. Schiffman '44 Geotechnical Colloquium
Cornell University - Civil & Environmental Engineering

## Slide 2
USS Intrepid

## Slide 3: USS Intrepid in 1971

## Slide 4
Solomon Cady Hollister (1891-1982)

## Slide 5
Prof. Mike
Jamiolkowski
Prof. Paul
Mayne
Prof. Mehmet
Tumay
Prof. Bob
Schiffman

## Slide 6: Purposes: Geotechnical Site Investigation
A must prior to all geotechnical projects
Determine geostratigraphy for site development
Obtain information for construction and foundation selection or ground modification
Collect geotechnical data for parameter evaluation
Input to analytical models and numerical FEM
Minimize surprises during construction
Mitigate potential for legal involvement

## Slide 7: Geomaterial Characteristics

## Slide 8
UD
tube
Dynamic Penetration
SPT:
N60
f'
DR
Vane Shear (VST):
suv = shear strength
St = sensitivity
Crosshole
CHT
Vs, Vp
Gmax
FIRM CLAY
DENSE
SAND
CONVENTIONAL DRILLING
& SAMPLING
Seismograph
Pressuremeter (PMT)
P0 = lateral stress
G’ = shear modulus
suPMT = shear strength
PL = limit pressure
SOILS LABORATORY
TX = triaxial shear
CS = consolidation
DSS = direct simple shear
RC = resonant column
PM = permeameter
TX CS RC PM
BEST APPROACH
DSS
CPT
DMT
Pump tests
TEXAM
IN-SITU
GEOPHYSICS

## Slide 9
Sieves
Hyd
Tv
Grain size analyses
Hydrometer
Water content by oven
Liquid limit cup
Plastic limit thread
Fall cone device
Pocket penetrometer
Torvane
Unconfined compression
Miniature vane
Digital image analysis
Mechanical oedometer
Consolidometer
Constant rate of shear (CRS)
Falling-head permeameter
Constant-head permeameter
Flow permeameter
Direct shear box
Ring shear
Unconsolidated undrained Tx
Simple shear
Directional shear cell
Triaxial apparatus (iso-consols, CIUC, CKoUC, CAUC, CIUE, CAUE, CKoUE, stress path, CIDC, CKoDC, CIDE, CKoDE, constant P’)
Plane strain apparatus (PSC, PSE)
True triaxial (cuboidal)
Hollow cylinder
Torsional Shear
Resonant Column Test device
Non-resonant column
Bender elements
Mechanical Laboratory Testing Methods
Pp
wn
Cup
Oed
Fall
Cone
Vst
DSB
DSS
RS
Permeameters
Consolidometers
UC
TTx
PSC PSE
DSC
HC RCT
Iso
Consol
CIUC
CIDC
CKoUC
CKoDC
CKoUE
CKoDE
CIUE
CIDE
BE
Pan

## Slide 10: Laboratory Soils Testing
  Limited number (discrete points)
  Lengthy test durations
  Affected by sample disturbance
  Expensive: Cost per specimen:
    Oedometer = $600 (2 weeks)
    Automated Consolidation = $800 (2-3 days)
    CIUC Triaxial = $600 (2 to 3 days)
    CK0UC Triaxial = $1500 ea (5 days)
    Resonant Column= $2000 ea (1 week)
    Permeability = $800 (1 to 2 weeks)
Sampler A Sampler B
Varved Clay

## Slide 11: Geotechnical Methods for Site Investigation
Soils Laboratory
Lab Rat

## Slide 12
SPT
TxPT
LPT
VST
PMT
CPMT
DMT
SPLT
K0SB
SWS
HF
BST
TSC
FTS
CPT
CPTu
RCPTu
SCPTu
SDMT
TBPT
BPT
Full Flow Penetrometers
SPTT
SCPMTù
SPT = Standard Penetration Test
TxPT = Texas Penetration Test
VST = Vane Shear Test
PMT = Pressuremeter Test
CPMT = Cone Pressuremeter
DMT = Dilatometer Test
SPLT = Screw Plate Load Test
ISB = Iowa K0 Stepped Blade
SWS = Swedish Weight Sounding
HF = Hydraulic Fracture
BST = Borehole Shear Test
TSC = Total Stress Cell (spade cell)
FTS = Freestand Torsional Shear
PV = Piezovane
MPT = Macintosh Probe Test
CPT = Cone Penetration Test
CPTu = Piezocone Penetration
RCPTu = Resistivity Piezocone
SCPTu = Seismic Cone
SDMT = Seismic Flat Dilatometer
TBPT = T-Bar Penetrometer Test
BPT = Ball Penetrometer
PPT = Plate Penetration Test
PLT = plate load test
HPT = Helical Probe Test
PBPT = piezoball penetration test
RapSochs = Rapid soil characterization system
CPTù = piezodissipation test
DMTà = Dilatometer test with A-reading dissipations
SPTT = Standard Penetration Test with Torque
LPT = Large Penetration Test
DEPPT = Dual Element PiezoProbe Test
SCPMTu = Seismic Piezocone Pressuremeter
PLT
DEPPT
HPT
Field Geotechnical In-Situ Testing Methods
PPT
MPT
PV
PBPT
RapSochs
CPTù
DMTà

## Slide 13: Cone Penetrometer Test (CPT)
Electronic Steel Probes with 60° Apex Tip
ASTM D 5778 Procedures
Hydraulic Push at 20 mm/s
No Boring, No Samples, No Cuttings, No Spoil
Continuous readings of stress, friction, pressure
Immediate access to digital data

## Slide 14: Geostratigraphy by CPTu in Portsmouth, Virginia

## Slide 15: CPT
Current Phase Tranformer
Cross Product Team
Cellular Paging Teleservice
Chest Percussion Therapy
Crisis Planning Team
Consumer Protection Trends
Computer Placement Test
Current Procedural Terminology
Cost Per Treatment
Choroid Plexus Tumor
Cardiopulmonary Physical Therapy
Corrugated Plastic Tubing
Cumulative Price Threshold
Cell Prepartion Tube
Central Payment Tool
Certified Proctology Technologist
Cockpit Procedures Trainer
Color Picture Tube
Critical Pitting Temperature
Certified Phelbotomy Technician
Control Power Transformer
Cone Penetration Test
Cost Production Team
Channel Product Table
Conditional Probability Table
Command Post Terminal

## Slide 16: Repeatability of CPTs Chalmette Levees, New Orleans
Location LPV 146-53c

## Slide 17: CPTu from Blytheville, Missouri
5 MPa (50 tsf)
SAND
CLAY

## Slide 18: Cone Penetrometers
10-cm2
15-cm2
mechanical
electric
cabled
piezo-
electronic
seismic-
digital
wireless

## Slide 19
10 cm2 10 cm2 15 cm2 15 cm2
10 cm2
5 cm2
1 cm2
15 cm2
Cone Penetrometer Sizes
2 cm2 10 cm2
d = 35 mm d = 44 mm

## Slide 20: Cone Penetrometer Sizes
33 cm2
10 cm2
15 cm2
Fugro
Penetrometers
ConeTec
Group

## Slide 21: CPT'10 - Summary Regional Reports
Harpoon Type Cone Penetrometers
US Navy XDP
Canadian FFCPT
German MARUM
Australian FFP
"Free-Fall Cone Penetration Test"
44 mm < d < 168 mm

## Slide 22: CPT'10 - Summary Regional Reports
CPT Probes for Centrifuge - Univ. Western Australia
Drum Centrifuge
Main Centrifuge
0 50 mm
T-bar
Ball
Plate
Mini-Cone Penetrometers

## Slide 23: Micro-Cone Penetrometers
Kim, Choi, Lee & Lee: Korea University
(GeoFlorida 2010)
FBG = Fibre Bragg Grating sensor

## Slide 24: Cone Penetration Vehicles
InDOT

## Slide 25: Cone Penetration Vehicles

## Slide 26: Georgia Tech Anchored Cone Rig
6-tonne CPT truck with 20-tonne hydraulic pushing system
No special license
Twin earth anchors
Has been used at sites in GA, VA, NC, SC, IL, FL, AR, MO, TN, KY, and AL
Downtown Atlanta, Georgia

## Slide 27: Geotechnical Site Characterization
Soils Laboratory vs In-Situ Testing
Lab Rat Field Mouse

## Slide 28: Cone Penetrometer Rigs

## Slide 29
AutoCoson - Robotic CPT
by A.P. van den Berg, Holland
PROD = Portable Remotely Operated Drill
by Benthic Geotech Australia

## Slide 30: Special CPTs
Resistivity Cones
Seismic CPT
Conductivity CPT
Gamma CPT
pH CPTu
Vision CPT (VisCPT)
Dielectric CPTu
Acoustic CPT
Radio-isotope CPT
Vibrocone (VCPT)

## Slide 31: Specialty Cone Penetrometers
VisCPT = vision penetrometer (Hryciw 2004)
Clean
Sand
Silty
Sand
Silty
fine
Sand
Silty
Clay
Visual data
acquisition
recording
system
Sapphire
window

## Slide 32: Cone Penetrometer Testing
Chinese CPT Equipment
www.madeinchina.com
圆锥贯入试验

## Slide 33: Cone Penetrometer Testing
Hand-held electronic cone penetrometers
Rimik CP40
Measured Penetration Resistance
Excellent Repeatability
Spectrum
Scout SC 900
Eijkelcamp

## Slide 34: CPT'10 - Summary Regional Reports
CPTs Halley Research Station - Antarctica

## Slide 35: CPT'10 - Summary Regional Reports
Adrian McCallum
Scott Polar Research Institute (SPRI)
Lankelma, UK
CPTs to Measure Strength of Polar Ice - Antarctica
Cone Resistance, qc (MPa)
0 2 4 6 8 10 12 14
Depth (meters)
0
1
2
3
4

## Slide 36: Earth
CPTs
all 7 continents
all 5 oceans

## Slide 37: Mars

## Slide 38
Launched May 2018
Landed November 2018

## Slide 39: External Geotechnical Review Team (23 Jan 2013)
Martian
Penetrometer

## Slide 40: Interpretation Methods for In-Situ Tests
Empirical
Analytical
Statistical
Dislocation Theory

## Slide 41: Interpretation Methods for In-Situ Tests
Finite Elements
Strain Path Method
Finite Differences
Discrete Elements

## Slide 42: CPT Computer Programs for Interpretation
GEO5 Pile CPT (gintsoftware)
GLAMCPT (Omer 2006)
CPeT-IT (geologismiki.gr)
LPD-CPT (Louisana State University)
Conrad (Swedish Geotech Institute)
CPTINT (Dick Campanella)
CPTLiq (Geosoftwaresolutions)
CPT-Log (Geotech.se)
DCCONE (dc-software.com)
Edison - SGI
MFoundation (GeoDelft)
CPT-Pro (www.geosoft.com.pl)
P-Class - (LSU and LTRC, Louisiana)
PL-aid (McTrans at Univ. Florida)
RapidCPT (dataforensics.net)
Shake2000 (CPT for soil liquefaction)
Static Probing (www.geostru.com)
Unipile (www.unisoftltd.com)
Georit (Geotech AB)
CPT7 (GeoMil Equipment)
ScreenZw (ConeTec)
CPTGL (Geotech AB reduction)
Go! (van den Berg)
Almeid (UWA)
CPTPlot
CLiq (geologismiki.gr)
GeoExplorer (Gouda-Geo Equip)
SPAS 2009 (geologismiki.gr)
INSITU (www.geo&soft.com)
OpenSounding (sourceforge.net)
PCL-pro (Geotech)
PlotCPT (GeoMil Equipment)
SCPT-DAA (Baziw)
Static Penetrometer (Alpes-Geo)
LCPC360A (ConeTec)
FB-Deep (Univ. of Florida)
Gorilla (A.P. van den Berg)
NovoCPT 1.2 (novosoftware.com)

## Slide 43: Recent advancements in interpretation
Geostratigraphy and soil type
Initial state and geostatic stresses
Relative density, DR
Unit weight, gt
Yield stress, sp' and YSR = yield stress ratio
Effective stress friction angle, f'
Rigidity index, IR = G/su
Undrained shear strength, su
Small-strain stiffness, Gmax
Stress-strain-strength response: t-g-tmax
Permeability (k) and coefficient of consolidation, cv
Direct methods for shallow footing foundations
Direct CPT methods for deep foundations
State parameter, y
Flow and cyclic liquefaction evaluation

## Slide 44: CPT Charts for Soil Behavioral Type
Soil Behavioral Type (SBT) charts (Robertson, CGJ, 1990, 1991)
Uses all 3 readings (qt, fs, u2)
Define normalized piezocone parameters:
1. Normalized Tip Resistance: Q = (qt - svo)/svo'
2. Normalized Sleeve Friction (%): F = 100  fs/(qt - svo)
3. Normalized Porewater Pressure: Bq = (u2-u0)/(qt - svo)
4. Updated Qtn = (qt - svo)/(svo')n where units of atm (≈ tsf)
with n = 1 clay and n = 0.5 in sand (Robertson 2009, 2016)

## Slide 45
Chart: CPT Soil Behavior Type
Zone 9 | 85 | 200 | 300 | 400 | 500 | 600 | 800 | 1000 | 1200
Gravelly SANDS
(Zone 7)
SANDS
(Zone 6)
Sandy Mix
(Zone 5)
Silty Mix
(Zone 4)
CLAYS
(Zone 3)
Organic
(Zone 2)
Sensitive Soils
(Zone 1)
Stiff
clayey
Sand
(Zone 8)
Very
Stiff
clays
and
silts
(Zone 9)
Robertson
(1990, 1991)
Canadian
Geotechnical
Journal

## Slide 46: Soil Behavioral Type Using CPT Index, Ic
Use of CPT Material Index (Ic) for identification of soil type (Robertson & Wride, 1998):
Modified normalized tip resistance (Robertson 2004):
Exponent n = 0.5 (sands), 0.75 (silts), n = 1.0 (clays)
Iterate to find exponent n (Robertson 2009 CGJ):
sands: Ic < 2.05
clays: Ic > 2.95

## Slide 47
Soil Behavioral
Type (SBTn) Chart
for normalized CPT
(after Robertson 2009)
a. Find sensitive soils of zone 1 identified when: Qtn < 12 exp(-1.4 Fr )
b. Identify: Zone 8 (1.5 < Fr< 4.5%) and Zone 9 (Fr > 4.5%):
c. Use CPT index Ic for Zones 2 through 7
Approximate
Algorithm Steps:
Ic < 2.6: Drained
Ic > 2.6: Undrained

## Slide 48: Undisturbed Sand Database
24 Sands to Silty Sands (n = 54 Triaxial Tests)

## Slide 49: Direct CPT method for f' in sands
Exponent
n ≈ ½

## Slide 50: Direct CPT method for f' in sands
32°
45°
Range
of f'

## Slide 51: Triaxial Compression Tests on Korean Soft Clay Drained and Undrained Series
Chart: Mean Effective Stress, p' (kPa)
| 200 | 197.435897435897 | 189.74358974359001 | 184.61538461538501 | 174.358974358974 | 161.538461538462 | 151.28205128205099 | 138.461538461538 | 133.333333333333 | 125.641025641026 | 117.948717948718 | 112.820512820513 | 107.69230769230801 | 102.564102564103 | 97.435897435897402 | 94.871794871794904 | 87.179487179487197 | 82.051282051282101 | 300 | 297.435897435897 | 276.92307692307702 | 261.538461538462 | 246.15384615384599 | 225.641025641026 | 210.25641025640999 | 194.871794871795 | 184.61538461538501 | 174.358974358974 | 164.102564102564 | 156.41025641025601 | 153.84615384615401 | 143.58974358974399 | 138.461538461538 | 133.333333333333 | 130.769230769231 | 123.07692307692299 | 115.384615384615 | 402.564102564103 | 397.435897435897 | 374.35897435897402 | 348.71794871794901 | 328.20512820512801 | 302.564102564103 | 271.79487179487199 | 248.71794871794901 | 233.333333333333 | 212.82051282051299 | 200 | 192.30769230769201 | 184.61538461538501 | 174.358974358974 | 166.666666666667 | 161.538461538462 | 153.84615384615401 | 148.71794871794901 | 146.15384615384599
CIU | 0 | 15 | 40 | 52.5 | 65 | 75 | 85 | 90 | 95 | 97.5 | 100 | 102.5 | 102.5 | 105 | 105 | 102.5 | 100 | 92.5 | 0 | 17.5 | 57.5 | 77.5 | 87.5 | 105 | 115 | 125 | 132.5 | 140 | 142.5 | 142.5 | 145 | 147.5 | 145 | 142.5 | 140 | 135 | 130 | 0 | 22.5 | 75 | 100 | 112.5 | 130 | 145 | 155 | 162.5 | 170 | 172.5 | 175 | 177.5 | 175 | 175 | 172.5 | 167.5 | 160 | 157.5
mC | 0 | 880
(Lee et al. 2000)
Notes: bigg

## Slide 52
Triaxial Compression Piezocone Penetrometer
Deviator Stress
q = sv - sh
Cell Pressure
Valve
pore pressure, u
qt
u2
sh
cone
resistance
porewater
pressure
Test one specimen
Soil Column
z > 30m
Billions of soil particles tested
sh
Principle of effective stress: s' = s - u
Triaxial
Cell
Notes: L: TX cell one point R: CPTu test infinite number of soil particles Put q on the TX part for CPTu, put qt, u2 bigger and full name

## Slide 53: Effective Stress Friction Angle f' from CPTu
qnet = (Nq - 1)∙(svo' + a') - Nu ∙Du2 = qt - svo
Nq = tan2(45°+f'/2)∙exp[(p-2b)∙tanf']
Nu = 6∙tanf'∙(1+tanf')
a' = c'∙cotf' = attraction
b = angle of plastification
Norwegian Institute of
Technology (NTH); NTNU
Janbu & Senneset (1974)
Senneset et al. (1982)
Senneset & Janbu (1985)
Sandven et al. (1988)
Senneset et al. (1988)
Senneset & Janbu (1989)
Sandven (1990)
Sandven & Watn (1995)
Sandven et al. (2016)
Ouyang & Mayne (2018)
f' in all soil types

## Slide 54: Effective Stress Piezocone Penetration
NTH: Sandven (1995), Senneset, Sandven, and Janbu (1989)
Chart: Effective Friction Angle, f' (degrees)
| 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63
Bq = 0.1 | 2.4428 | 2.7303 | 3.0428 | 3.3832 | 3.7543 | 4.1596 | 4.6028 | 5.0882 | 5.6207 | 6.2059 | 6.8501 | 7.5605 | 8.3454 | 9.2144 | 10.1784 | 11.2501 | 12.4442 | 13.7779 | 15.2712 | 16.9474 | 18.8341 | 20.9637 | 23.3749 | 26.1133 | 29.2337 | 32.8019 | 36.8972 | 41.6158 | 47.0751 | 53.419 | 60.8252 | 69.5141 | 79.7615 | 91.9144 | 106.4133 | 123.8215 | 144.8653 | 170.4907 | 201.9406 | 240.8663 | 289.4857 | 350.8138 | 429.0029 | 529.8511 | 661.579 | 836.0329 | 1070.592 | 1391.2524 | 1837.735
Bq = 0.2 | 2.0891 | 2.3113 | 2.5501 | 2.807 | 3.084 | 3.3832 | 3.7069 | 4.0579 | 4.4391 | 4.854 | 5.3065 | 5.8011 | 6.3428 | 6.9374 | 7.5916 | 8.313 | 9.1106 | 9.9946 | 10.9769 | 12.0716 | 13.2949 | 14.6661 | 16.2079 | 17.9471 | 19.9159 | 22.1525 | 24.7031 | 27.6234 | 30.981 | 34.8589 | 39.3586 | 44.6061 | 50.7583 | 58.012 | 66.616 | 76.8874 | 89.2339 | 104.1842 | 122.431 | 144.8912 | 172.7921 | 207.7963 | 252.1858 | 309.1362 | 383.1342 | 480.6237 | 611.0256 | 788.3842 | 1034.0857
Bq = 0.4 | 1.62 | 1.7686 | 1.9262 | 2.0938 | 2.2725 | 2.4635 | 2.6682 | 2.8882 | 3.1251 | 3.381 | 3.658 | 3.9587 | 4.2858 | 4.6428 | 5.0332 | 5.4614 | 5.9322 | 6.4515 | 7.0257 | 7.6625 | 8.371 | 9.1617 | 10.0469 | 11.0414 | 12.1626 | 13.4314 | 14.8727 | 16.5167 | 18.3999 | 20.567 | 23.0728 | 25.9847 | 29.3868 | 33.3845 | 38.1104 | 43.7335 | 50.4704 | 58.6019 | 68.4946 | 80.6333 | 95.6654 | 114.4665 | 138.2358 | 168.6393 | 208.0263 | 259.7646 | 328.7686 | 422.3512 | 551.6276
Bq = 0.6 | 1.3229 | 1.4323 | 1.5476 | 1.6696 | 1.7991 | 1.937 | 2.0842 | 2.2419 | 2.4113 | 2.5938 | 2.7909 | 3.0044 | 3.2363 | 3.4888 | 3.7645 | 4.0664 | 4.3979 | 4.763 | 5.1661 | 5.6126 | 6.1086 | 6.6615 | 7.2797 | 7.9734 | 8.7545 | 9.6373 | 10.639 | 11.7801 | 13.0859 | 14.5866 | 16.3199 | 18.3318 | 20.6797 | 23.4355 | 26.6896 | 30.5572 | 35.1857 | 40.766 | 47.5477 | 55.8599 | 66.1424 | 78.9892 | 95.2136 | 115.9446 | 142.7732 | 177.9787 | 224.8852 | 288.4356 | 376.1383
Bq = 0.8 | 1.1179 | 1.2035 | 1.2934 | 1.3884 | 1.489 | 1.5959 | 1.71 | 1.832 | 1.963 | 2.104 | 2.2562 | 2.4209 | 2.5997 | 2.7943 | 3.0067 | 3.2391 | 3.4942 | 3.775 | 4.0849 | 4.428 | 4.8089 | 5.2334 | 5.7077 | 6.2396 | 6.8383 | 7.5146 | 8.2815 | 9.1548 | 10.1535 | 11.3007 | 12.6249 | 14.1611 | 15.953 | 18.0549 | 20.5356 | 23.4823 | 27.0068 | 31.2538 | 36.4122 | 42.7313 | 50.5441 | 60.3 | 72.6143 | 88.3407 | 108.6821 | 135.3609 | 170.8884 | 218.9977 | 285.3575
Bq = 1.0 | 0.96789 | 1.0377 | 1.1109 | 1.1882 | 1.27 | 1.357 | 1.4497 | 1.5488 | 1.6552 | 1.7698 | 1.8934 | 2.0272 | 2.1724 | 2.3304 | 2.5028 | 2.6915 | 2.8986 | 3.1265 | 3.3779 | 3.6563 | 3.9653 | 4.3095 | 4.694 | 5.1252 | 5.6103 | 6.1582 | 6.7793 | 7.4864 | 8.2947 | 9.223 | 10.2942 | 11.5365 | 12.985 | 14.6837 | 16.6878 | 19.0676 | 21.9131 | 25.3408 | 29.5027 | 34.5995 | 40.899 | 48.7626 | 58.6852 | 71.3531 | 87.7333 | 109.21 | 137.8012 | 176.5057 | 229.8768
 | 6.4522 | 11.4098 | 19.9925 | 27.6303 | 34.6882 | 41.3329 | 47.6595 | 53.7293 | 59.5849 | 65.2575 | 70.7707 | 76.1435 | 81.3907 | 86.5246 | 91.5557 | 96.4926 | 101.3428 | 106.1127 | 110.8079 | 115.4335 | 124.4925 | 133.3197 | 141.9392 | 150.3709 | 158.6317 | 178.6241 | 197.8062 | 216.3038 | 234.2115 | 251.6026 | 268.5356 | 285.0579 | 301.2089 | 317.0218

## Slide 55: Soft Clay at Northwestern University
qt
u2

## Slide 56
Nm = Q = 3.05

## Slide 57
Bq = 0.79

## Slide 58: Soft Clay at Northwestern University
Chart: Effective Friction Angle, f' (degrees)
| 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63
Bq = 0.1 | 2.4428 | 2.7303 | 3.0428 | 3.3832 | 3.7543 | 4.1596 | 4.6028 | 5.0882 | 5.6207 | 6.2059 | 6.8501 | 7.5605 | 8.3454 | 9.2144 | 10.1784 | 11.2501 | 12.4442 | 13.7779 | 15.2712 | 16.9474 | 18.8341 | 20.9637 | 23.3749 | 26.1133 | 29.2337 | 32.8019 | 36.8972 | 41.6158 | 47.0751 | 53.419 | 60.8252 | 69.5141 | 79.7615 | 91.9144 | 106.4133 | 123.8215 | 144.8653 | 170.4907 | 201.9406 | 240.8663 | 289.4857 | 350.8138 | 429.0029 | 529.8511 | 661.579 | 836.0329 | 1070.592 | 1391.2524 | 1837.735
Bq = 0.2 | 2.0891 | 2.3113 | 2.5501 | 2.807 | 3.084 | 3.3832 | 3.7069 | 4.0579 | 4.4391 | 4.854 | 5.3065 | 5.8011 | 6.3428 | 6.9374 | 7.5916 | 8.313 | 9.1106 | 9.9946 | 10.9769 | 12.0716 | 13.2949 | 14.6661 | 16.2079 | 17.9471 | 19.9159 | 22.1525 | 24.7031 | 27.6234 | 30.981 | 34.8589 | 39.3586 | 44.6061 | 50.7583 | 58.012 | 66.616 | 76.8874 | 89.2339 | 104.1842 | 122.431 | 144.8912 | 172.7921 | 207.7963 | 252.1858 | 309.1362 | 383.1342 | 480.6237 | 611.0256 | 788.3842 | 1034.0857
Bq = 0.4 | 1.62 | 1.7686 | 1.9262 | 2.0938 | 2.2725 | 2.4635 | 2.6682 | 2.8882 | 3.1251 | 3.381 | 3.658 | 3.9587 | 4.2858 | 4.6428 | 5.0332 | 5.4614 | 5.9322 | 6.4515 | 7.0257 | 7.6625 | 8.371 | 9.1617 | 10.0469 | 11.0414 | 12.1626 | 13.4314 | 14.8727 | 16.5167 | 18.3999 | 20.567 | 23.0728 | 25.9847 | 29.3868 | 33.3845 | 38.1104 | 43.7335 | 50.4704 | 58.6019 | 68.4946 | 80.6333 | 95.6654 | 114.4665 | 138.2358 | 168.6393 | 208.0263 | 259.7646 | 328.7686 | 422.3512 | 551.6276
Bq = 0.6 | 1.3229 | 1.4323 | 1.5476 | 1.6696 | 1.7991 | 1.937 | 2.0842 | 2.2419 | 2.4113 | 2.5938 | 2.7909 | 3.0044 | 3.2363 | 3.4888 | 3.7645 | 4.0664 | 4.3979 | 4.763 | 5.1661 | 5.6126 | 6.1086 | 6.6615 | 7.2797 | 7.9734 | 8.7545 | 9.6373 | 10.639 | 11.7801 | 13.0859 | 14.5866 | 16.3199 | 18.3318 | 20.6797 | 23.4355 | 26.6896 | 30.5572 | 35.1857 | 40.766 | 47.5477 | 55.8599 | 66.1424 | 78.9892 | 95.2136 | 115.9446 | 142.7732 | 177.9787 | 224.8852 | 288.4356 | 376.1383
Bq = 0.8 | 1.1179 | 1.2035 | 1.2934 | 1.3884 | 1.489 | 1.5959 | 1.71 | 1.832 | 1.963 | 2.104 | 2.2562 | 2.4209 | 2.5997 | 2.7943 | 3.0067 | 3.2391 | 3.4942 | 3.775 | 4.0849 | 4.428 | 4.8089 | 5.2334 | 5.7077 | 6.2396 | 6.8383 | 7.5146 | 8.2815 | 9.1548 | 10.1535 | 11.3007 | 12.6249 | 14.1611 | 15.953 | 18.0549 | 20.5356 | 23.4823 | 27.0068 | 31.2538 | 36.4122 | 42.7313 | 50.5441 | 60.3 | 72.6143 | 88.3407 | 108.6821 | 135.3609 | 170.8884 | 218.9977 | 285.3575
Bq = 1.0 | 0.96789 | 1.0377 | 1.1109 | 1.1882 | 1.27 | 1.357 | 1.4497 | 1.5488 | 1.6552 | 1.7698 | 1.8934 | 2.0272 | 2.1724 | 2.3304 | 2.5028 | 2.6915 | 2.8986 | 3.1265 | 3.3779 | 3.6563 | 3.9653 | 4.3095 | 4.694 | 5.1252 | 5.6103 | 6.1582 | 6.7793 | 7.4864 | 8.2947 | 9.223 | 10.2942 | 11.5365 | 12.985 | 14.6837 | 16.6878 | 19.0676 | 21.9131 | 25.3408 | 29.5027 | 34.5995 | 40.899 | 48.7626 | 58.6852 | 71.3531 | 87.7333 | 109.21 | 137.8012 | 176.5057 | 229.8768
 | 6.4522 | 11.4098 | 19.9925 | 27.6303 | 34.6882 | 41.3329 | 47.6595 | 53.7293 | 59.5849 | 65.2575 | 70.7707 | 76.1435 | 81.3907 | 86.5246 | 91.5557 | 96.4926 | 101.3428 | 106.1127 | 110.8079 | 115.4335 | 124.4925 | 133.3197 | 141.9392 | 150.3709 | 158.6317 | 178.6241 | 197.8062 | 216.3038 | 234.2115 | 251.6026 | 268.5356 | 285.0579 | 301.2089 | 317.0218
b = 0
Q = 3.05
Bq = 0.79
f’ = 28.8°

## Slide 59: Soft Clay at Northwestern University
CAUC Triaxial Test Series

## Slide 60: Approximate NTH Solution for f' from CPTu
Approx: f' ≈ 29.5°∙Bq0.121∙[0.256 + 0.336∙Bq + log Q ]
Chart: f' (degrees)
| 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63
Bq = 0.1 | 2.4428 | 2.7303 | 3.0428 | 3.3832 | 3.7543 | 4.1596 | 4.6028 | 5.0882 | 5.6207 | 6.2059 | 6.8501 | 7.5605 | 8.3454 | 9.2144 | 10.1784 | 11.2501 | 12.4442 | 13.7779 | 15.2712 | 16.9474 | 18.8341 | 20.9637 | 23.3749 | 26.1133 | 29.2337 | 32.8019 | 36.8972 | 41.6158 | 47.0751 | 53.419 | 60.8252 | 69.5141 | 79.7615 | 91.9144 | 106.4133 | 123.8215 | 144.8653 | 170.4907 | 201.9406 | 240.8663 | 289.4857 | 350.8138 | 429.0029 | 529.8511 | 661.579 | 836.0329 | 1070.592 | 1391.2524 | 1837.735
Bq = 0.2 | 2.0891 | 2.3113 | 2.5501 | 2.807 | 3.084 | 3.3832 | 3.7069 | 4.0579 | 4.4391 | 4.854 | 5.3065 | 5.8011 | 6.3428 | 6.9374 | 7.5916 | 8.313 | 9.1106 | 9.9946 | 10.9769 | 12.0716 | 13.2949 | 14.6661 | 16.2079 | 17.9471 | 19.9159 | 22.1525 | 24.7031 | 27.6234 | 30.981 | 34.8589 | 39.3586 | 44.6061 | 50.7583 | 58.012 | 66.616 | 76.8874 | 89.2339 | 104.1842 | 122.431 | 144.8912 | 172.7921 | 207.7963 | 252.1858 | 309.1362 | 383.1342 | 480.6237 | 611.0256 | 788.3842 | 1034.0857
Bq = 0.4 | 1.62 | 1.7686 | 1.9262 | 2.0938 | 2.2725 | 2.4635 | 2.6682 | 2.8882 | 3.1251 | 3.381 | 3.658 | 3.9587 | 4.2858 | 4.6428 | 5.0332 | 5.4614 | 5.9322 | 6.4515 | 7.0257 | 7.6625 | 8.371 | 9.1617 | 10.0469 | 11.0414 | 12.1626 | 13.4314 | 14.8727 | 16.5167 | 18.3999 | 20.567 | 23.0728 | 25.9847 | 29.3868 | 33.3845 | 38.1104 | 43.7335 | 50.4704 | 58.6019 | 68.4946 | 80.6333 | 95.6654 | 114.4665 | 138.2358 | 168.6393 | 208.0263 | 259.7646 | 328.7686 | 422.3512 | 551.6276
Bq = 0.6 | 1.3229 | 1.4323 | 1.5476 | 1.6696 | 1.7991 | 1.937 | 2.0842 | 2.2419 | 2.4113 | 2.5938 | 2.7909 | 3.0044 | 3.2363 | 3.4888 | 3.7645 | 4.0664 | 4.3979 | 4.763 | 5.1661 | 5.6126 | 6.1086 | 6.6615 | 7.2797 | 7.9734 | 8.7545 | 9.6373 | 10.639 | 11.7801 | 13.0859 | 14.5866 | 16.3199 | 18.3318 | 20.6797 | 23.4355 | 26.6896 | 30.5572 | 35.1857 | 40.766 | 47.5477 | 55.8599 | 66.1424 | 78.9892 | 95.2136 | 115.9446 | 142.7732 | 177.9787 | 224.8852 | 288.4356 | 376.1383
Bq = 0.8 | 1.1179 | 1.2035 | 1.2934 | 1.3884 | 1.489 | 1.5959 | 1.71 | 1.832 | 1.963 | 2.104 | 2.2562 | 2.4209 | 2.5997 | 2.7943 | 3.0067 | 3.2391 | 3.4942 | 3.775 | 4.0849 | 4.428 | 4.8089 | 5.2334 | 5.7077 | 6.2396 | 6.8383 | 7.5146 | 8.2815 | 9.1548 | 10.1535 | 11.3007 | 12.6249 | 14.1611 | 15.953 | 18.0549 | 20.5356 | 23.4823 | 27.0068 | 31.2538 | 36.4122 | 42.7313 | 50.5441 | 60.3 | 72.6143 | 88.3407 | 108.6821 | 135.3609 | 170.8884 | 218.9977 | 285.3575
Bq = 1.0 | 0.96789 | 1.0377 | 1.1109 | 1.1882 | 1.27 | 1.357 | 1.4497 | 1.5488 | 1.6552 | 1.7698 | 1.8934 | 2.0272 | 2.1724 | 2.3304 | 2.5028 | 2.6915 | 2.8986 | 3.1265 | 3.3779 | 3.6563 | 3.9653 | 4.3095 | 4.694 | 5.1252 | 5.6103 | 6.1582 | 6.7793 | 7.4864 | 8.2947 | 9.223 | 10.2942 | 11.5365 | 12.985 | 14.6837 | 16.6878 | 19.0676 | 21.9131 | 25.3408 | 29.5027 | 34.5995 | 40.899 | 48.7626 | 58.6852 | 71.3531 | 87.7333 | 109.21 | 137.8012 | 176.5057 | 229.8768
Approx 0.1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 35 | 40 | 45 | 50 | 60 | 70 | 80 | 90 | 100
Approx. 0.2 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 35 | 40 | 45 | 50 | 60 | 70 | 80 | 90 | 100
Approx. 0.4 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 35 | 40 | 45 | 50 | 60 | 70 | 80 | 90 | 100
Approx. 0.6 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 35 | 40 | 45 | 50 | 60 | 70 | 80 | 90 | 100
Approx. 0.8 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 35 | 40 | 45 | 50 | 60 | 70 | 80 | 90 | 100
Approx. 1.0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 35 | 40 | 45 | 50 | 60 | 70 | 80 | 90 | 100
c' = 0
b = 0°
Theory (dots)
Approximation (lines)
Theory:

## Slide 61: Boston Blue Clay at Newbury, Massachusetts (Landon, 2007, Univ. Mass - Amherst)
Chart: Cone Resistance, qt (kPa)
Chart: Pressure, u2 (kPa)
Chart: Effective f' (deg)
Average from CKoUC block and piston samples | 5.55 | 6.125 | 7.45 | 9.675
Mean CK0UC
of Block
and Piston
Samples
Approx
NTH Method
for CPTu

## Slide 62: Miniature CPTu in Clay Centrifuge Deposits (Ouyang and Mayne, CPT'18, Delft)
10mm Mini-Piezocone at UWA
Zhejiang University Centrifuge

## Slide 63
Database of Laboratory CAUC/CIUC Triaxial f’ Tests and Field CPTu in Clays
N = 105 Clays
(Ouyang & Mayne, CGJ 2018)

## Slide 64
Comparison of Triaxial f’ and NTH f’ from CPTu
Electronic
Piezocone
Penetrometers
Triaxial
Apparatus

## Slide 65
by Jeff Keane

## Slide 66
Chart: Clays Sample from Evergreen, North Carolina
| 9.5749999999999996E-5 | 1.532 | 2.9682499999999998 | 6.0322500000000003 | 11.96875 | 23.9375 | 47.875 | 95.75 | 191.5 | 95.75 | 47.875 | 23.9375 | 47.875 | 95.75 | 191.5 | 383 | 766 | 1532 | 383 | 0.95750000000000002
 | 1.9074 | 1.898 | 1.8922 | 1.8797 | 1.8591 | 1.8088 | 1.7111 | 1.5663 | 1.3962 | 1.4076 | 1.4271 | 1.4445 | 1.4398 | 1.4271 | 1.3657 | 1.1762 | 0.95229 | 0.75691 | 0.81099 | 1.1087
svo' = 43 kPa
sp' = 80 kPa
(most probable)
Benchmark: Yield Stress from Consolidation Tests
Casagrande Method (1936)

## Slide 67: Cavity Expansion-Critical State Model for CPTu-OCR
Clay Properties:
M = 6 sinf’/(3-sinf’)
f’ = effective friction angle
Cc = compression index
Cs = swelling index
L = 1 – Cs/Cc
IR = G/su = Rigidity Index
G = shear modulus
su = undrained shear strength
f’, Cc, Cs
Mayne (1991)
Chen & Mayne (1994)
Burns & Mayne (1998, 2002)
Mayne (2005, 2007)
Mayne (2017)

## Slide 68: SCE-CSSM Analytical Solution
Notes:
M = 6 sinf'/(3-sinf')
IR = G/su
L = 1 – Cs/Cc ≈ 0.80
(clays and sands)
qt
u2
Clays
Rigidity Index

## Slide 69
qt
u2
fs
THIS U2

## Slide 70: SCE-CSSM Theory
For L = 1
f’ = 30o and IR = 100
First-Order Approximations
for inorganic insensitive clays

## Slide 71: San Francisco Bay Mud Islais Creek (Hunt, Pestana, Bray - JGGE 2002)
Chart: Cone Resistance qt (kPa)
Chart: Sleeve Friction fs (kPa)
Chart: Pore Pressure u2 (kPa)
Chart: Effective Yield Stress sp' (kPa)
CRS | 8.5 | 12.8 | 23.8
Miscellaneous Fill
Young
Bay Mud
Young
Bay Mud
Clayey
Sand
qnet
qE
Du2
Clayey
Sand
Young
Bay Mud

## Slide 72
Bothkennar Test Site - Scotland
(Hight et al, 2003; Powell and Lunne, 2005)
Edinburgh

## Slide 73: Evaluating Yield Stresses in Sands by CPT
Oxford
University
Flexible Wall Chambers
Essentially large triaxial test
Virginia Tech
Calibration Chambers

## Slide 74: CPT Chamber Test Series on 26 Sands
Earlston
Edgar
Erksak
Frankston
Hilton Mines
Hokksund
Hostun
Lanchester
Leighton Buzzard
Light Castle Sand
Oosterschelde
Lone Star
Monterey
Ottawa
Reid-Bedford
South Oakleigh
Ticino
Toyoura
Washed Mortar Sand
Each Chamber ≈ 8 to 10 tons of sand
Takes one week to prepare by 3 personnel
Each CPT takes 20 seconds

## Slide 75: CPT Methodology in Clean Quartz Sands
Apparent Overconsolidation Ratio, OCR (or Yield Stress Ratio, YSR):
f’ = effective stress friction angle
qt = cone tip resistance
svo’ = effective vertical stress
satm = atmospheric pressure (1 bar = 100 kPa)

## Slide 76
CPT Calibration Chamber Test Data on Sands
Apparent Overconsolidation Ratio, OCR, or Yield Stress Ratio, YSR:
For f’ = 35°
First-Order
Approximation
where satm = atmospheric pressure (1 atm ≈ 1 bar = 100 kPa).
206 CLAY SITES
SANDS (706 chamber tests)
Units
of kPa

## Slide 77: Effective Yield Stress of Soils from CPT
Chart: Net Cone Resistance, qt - svo (kPa)
| 1 | 100000
Trend - Intact Clays | 0.33 | 33000
Trend - Silts | 0.33 | 5868.3221
Trend - Clean Sands | 0.33 | 1313.7537
Opelika Sandy Silt | 210 | 216.72 | 230.86 | 266.56 | 273
Stockholm Sand | 280 | 294 | 312 | 327 | 347 | 361 | 377 | 393
Vagverket Silt | 77.175 | 92.61 | 108.045 | 123.48 | 138.915 | 154.35 | 169.785 | 185.22 | 200.655 | 216.09
Po River Sand | 194.23 | 202.52 | 210.81 | 219.1 | 227.39 | 235.68 | 243.97 | 268.84 | 285.42 | 302
Sensitive Clays - Organics | 0.33 | 10435.5163
Pentre Silt | 177.1028 | 222.8022 | 268.5015 | 322.2183 | 359.0985 | 406.4013
Holmen Sand | 43.884 | 59.94 | 75.996 | 92.052 | 108.108 | 124.164 | 140.22 | 156.276 | 172.332
CLAYS
SILTS / MIXED
SANDS
sp' =0.33(qtnet)m

## Slide 78: Blessington Sand Site University of College Dublin (UCD)
Doherty et al. (2012)
Tolooiyan & Gavin (2011)

## Slide 79
Chart: Cone Resistance, qt (MPa)
Chart: Yield Stress Ratio, YSR
Consolidation Tests | 2.8696 | 1.7609 | 1.8261 | 1.7609 | 2.8696 | 5.6087 | 6.587 | 10.0435 | 9.9783 | 11.8696 | 13.8913 | 13.8913 | 11.9348
Consolidation
Tests
Dense
Fine
Sand
Dense OC Sand Site, Blessington, Ireland
(Dougherty et al. 2012; Gavin et al. 2014)

## Slide 80
Unified Approach: Yield Stress versus Net Cone Resistance
Robertson & Cabal (2015)

## Slide 81
Unified Approach: Evaluating Yield Stress of Various Different Geomaterials Using CPT

## Slide 82
Chart: Gravelly Sands Sandy Silty Clays Organic Sand Mix Mix
Hibernia Sand | 0.7
Euripides Sand | 0.78
Holmen Sand | 0.73
Po River Sand | 0.72
Blessington Sand | 0.74
Piedmont SM | 0.8
Piedmont ML | 0.83
Pentre Silt | 1
Vagverket Silt | 0.75
Mjardevi Silt | 0.8
Os Silt, Norway | 0.95
Fissured
Clays
Intact Clays
Silts
Quartz and
Silica Sands
CLAYS
SILTS
SANDS
For Ic < 3.5
Yield Stress Exponent m’ Trend with CPT Material Index, Ic
Zone No. = 7 6 5 4 3 2

## Slide 83
OC Sand at Cuxhaven, Germany (Quinteros et al. 2018)
Cuxhaven
North Sea

## Slide 84: OC Sand at Cuxhaven, Germany
(Quinteros, Lunne, Krogh, et al. CPT'18)
Calculated OCR due to 18 m of excavated overburden removal
Sand
Clay

## Slide 85: Shear Wave Velocity, Vs
Fundamental measurement in all solids (steel, concrete, wood, soils, rocks)
Initial stiffness represented by the small-strain shear modulus (Gdyn = Gmax = G0):
G0 = rt Vs2 where total mass density rt = gt/ga
Applies to all static & dynamic problems at small strains (gs < 10-6)
Applicable to both undrained & drained loading cases in geotechnical engineering

## Slide 86: Comparison MASW and DHT - Richmond, BC
Chart: Shear Wave Velocity, Vs (m/s)
| 95 | 95 | 61 | 61 | 74 | 74 | 104 | 104 | 102 | 102 | 133 | 133 | 140 | 140 | 147 | 147 | 168 | 168 | 231 | 231
MASW 11-1 | 0 | 0.45 | 0.45 | 1.02 | 1.02 | 1.72 | 1.72 | 2.61 | 2.61 | 3.71 | 3.71 | 5.09 | 5.09 | 6.82 | 6.82 | 8.97 | 8.97 | 11.66 | 11.66 | 14.58
Downhole Test | 0.9 | 1.9 | 1.9 | 2.9 | 2.9 | 3.9 | 3.9 | 4.9 | 4.9 | 5.9 | 5.9 | 6.9 | 6.9 | 7.9 | 7.9 | 8.9 | 8.9 | 9.9 | 9.9 | 11.9 | 11.9 | 12.9 | 12.9 | 13.9 | 13.9 | 14.9
200 m/s
Good
Bad

## Slide 87
Field Geophysics - Mechanical Wave Methods
SRFS = Surface Refraction Survey
SFLS = Surface Reflection Survey
SASW = Spectral Analysis of Surface Waves
MASW = Modal Analysis (Rayleigh Waves)
CSW = Continuous Surface Waves
PSW = Passive Surface Wave Testing
ReMi = Reflection MicroSeis
SLP = Suspension Logger Problng
CHT = Crosshole Test
RCHT = Rotary Crosshole
DHT = Downhole Test
UHT = Uphole Test
SCPTu = Seismic Piezocone Test
SDMT = Seismic Flat Dilatometer Test
BTSD = Borehole Torsional Shear Device
Seismograph
+ Source
Receivers
Geophones
SFLS
SFRS
Rotary
Source
Vertical
Source
Torsional
Source
Cased
Boreholes
VsHV
VsHH
VsHH
VsHH
Oscilloscope
+ Source
Vp
VsVH
Spectral
Analyzer
+ Source
SASW
MASW
CSW
PSW
ReMi
Rayleigh Wave Methods
CHT
RCHT
BTSD
SLP
VsVV
high frequencies
medium frequency
content
low
frequency
content
VsRW
DHT
UHT

## Slide 88
Seismic Piezocone Penetration Testing (SCPTu)
D 7400

## Slide 89: SCPTu at Meramac River, Missouri
Cone Resistance Sleeve Friction Pore Pressure Shear Wave Velocity
Vs
fs
u2
qt

## Slide 90: Costs of Methods to profile Vs to 30 m
METHOD | TYPICAL COST
Suspension Logging (PSSL) | $ 9,000
Crosshole Testing (CHT) | $ 22,000
Downhole Testing (DHT) | $ 9,000
Surface Waves (SASW, MASW) | $ 4,500
ReMi Passive Surface Waves | $ 2,500
Seismic Piezocone* | $ 2,000
NOTE:
* Includes 4 separate readings with depth: qt, fs, u2, and Vs

## Slide 91: Seismic Piezocone (SCPTU) - Ithaca, NY
Depth (feet)
Cone Resistance
qt (tsf)
Sleeve Friction
fs (tsf)
Pore Pressure
u2 (feet)
Shear Wave
Vs (fps)
Soil Behavior
Type (SBT)

## Slide 92: Geotechnical Methods for Site Investigation
Soils Laboratory In-Situ Testing
Lab Rat Field Mouse
Field mouse with
ball penetrometer
Geophysics
Fruit Bat

## Slide 93: SCPTu from Perth, Australia
(Schneider, et al. 2004; Low et al. 2011)
Burswood
Soft
Clay

## Slide 94: Soil Parameter Evaluation at Burswood by SCPTu
(Data from Univ. Western Australia: Schneider 2004; Low 2009)
Chart: Preconsolidation Stress, sp' (kPa)
Lab CRSC | 18.35 | 11.4 | 5.97 | 6.33 | 12.11 | 10 | 10 | 8.22 | 8.22 | 13.75 | 14.94 | 4.11 | 2.54 | 11.4
Chart: Undrained Shear Strength su (kPa)
Lab DSS | 4.7111 | 5.9579 | 9.4432 | 10.5667 | 12.6468 | 14.9566 | 3.8126 | 6.1766 | 6.6285 | 7.7523 | 8.4294 | 9.1573 | 10.3404 | 11.3542 | 12.753 | 13.0933 | 13.4353 | 14.5553

## Slide 95: DSS curves for Burswood by SCPTu
(Data from Low, 2004: Univ. Western Australia)
Chart: Shear Strain, γ (%)
| 0 | 0.16835016835016833 | 0.16835016835016833 | 0.16835016835016833 | 0.33670033670033667 | 0.50505050505050508 | 0.67340067340067333 | 0.67340067340067333 | 0.84175084175084169 | 0.84175084175084169 | 1.0101010101010102 | 1.1784511784511784 | 1.1784511784511784 | 1.5151515151515151 | 1.8518518518518516 | 2.0202020202020203 | 2.1885521885521886 | 2.3569023569023568 | 2.5252525252525251 | 2.6936026936026933 | 3.0303030303030303 | 3.3670033670033668 | 3.7037037037037033 | 4.0404040404040407 | 4.3771043771043772 | 4.7138047138047137 | 5.3872053872053867 | 5.8922558922558927 | 6.5656565656565666 | 7.2390572390572396 | 7.9124579124579126 | 8.9225589225589221 | 9.9326599326599325 | 11.111111111111111 | 11.784511784511785 | 12.457912457912458 | 14.309764309764308 | 15.31986531986532 | 17.003367003367003 | 18.350168350168349 | 19.36026936026936 | 20.53872053872054 | 21.71717171717172 | 22.895622895622896 | 24.242424242424242 | 25.589225589225588 | 27.27272727272727 | 28.787878787878789 | 29.797979797979796 | 31.649831649831651 | 32.996632996632997 | 34.848484848484851 | 36.531986531986533 | 38.215488215488215 | 39.73063973063973 | 40.404040404040401 | 41.07744107744108
CAU SS: 12.7 m | 0 | 3 | 5.3571 | 6.4286 | 7.3929 | 8.1429 | 9.9643 | 11.4643 | 12.3214 | 13.1786 | 13.8214 | 14.5714 | 15.4286 | 16.7143 | 18 | 18.5357 | 19.2857 | 20.1429 | 20.7857 | 21.4286 | 22.1786 | 22.8214 | 23.3571 | 24 | 24.4286 | 24.9643 | 25.6071 | 25.9286 | 26.4643 | 27 | 27.6429 | 28.0714 | 28.3929 | 28.3929 | 28.3929 | 28.1786 | 27.9643 | 27.9643 | 27.9643 | 27.5357 | 27.1071 | 26.8929 | 26.5714 | 26.25 | 25.9286 | 25.8214 | 25.6071 | 25.3929 | 25.1786 | 24.8571 | 24.75 | 24.75 | 24.4286 | 24.2143 | 24.1071 | 24.2143 | 24.1071
CAU SS: 14.9 m | 1.4774 | 2.7274 | 4.0911 | 5.114 | 5.8527 | 6.5914 | 7.6142 | 8.9779 | 9.8304 | 10.7395 | 11.9895 | 13.1829 | 14.2626 | 15.5128 | 16.4221 | 17.6153 | 18.5815 | 19.3206 | 20.0598 | 20.7422 | 21.5381 | 22.2203 | 22.7319 | 23.4142 | 23.8694 | 24.5518 | 25.1774 | 25.7462 | 26.3151 | 26.7136 | 26.7147 | 26.9998 | 27.2282 | 27.116 | 27.1745 | 27.2892 | 27.5744 | 27.6327 | 27.691 | 27.522 | 27.3528 | 27.4117 | 27.5833
CAU SS: 10.5 m | 0 | 5.3 | 8 | 10.7143 | 13.7 | 16.0714 | 18 | 19.3929 | 20.5714 | 21.4286 | 22.1786 | 22.9286 | 22.9286 | 23.0357 | 23.3571 | 23.5714 | 23.8929 | 24.1071 | 24.1071 | 24 | 23.8929 | 23.6786 | 23.4643 | 23.4643 | 23.3571 | 23.0357 | 22.8214 | 22.5 | 22.5 | 22.5 | 22.5 | 22.6071
CAU SS: 9.4 m | 0 | 3.8 | 6.5179 | 9.9107 | 12.0536 | 14.0179 | 15.3571 | 16.0714 | 16.7857 | 17.4107 | 18.0357 | 18.4821 | 18.8393 | 19.1071 | 19.375 | 19.5536 | 19.7321 | 19.9107 | 20.0893 | 20.1786 | 20.2679 | 20.4464 | 20.625 | 20.7143 | 20.8036 | 20.8036 | 20.8036 | 20.8036 | 20.8036 | 20.8036 | 20.7143 | 20.625 | 20.4464 | 20.3571 | 20.2679 | 20 | 19.8214 | 19.6429 | 19.375 | 19.1964 | 19.0179 | 18.9286 | 18.75 | 18.5714 | 18.3929 | 18.3036 | 18.2143 | 18.0357 | 17.9464 | 17.7679 | 17.6786 | 17.5
CAU SS: 4.8 m | 0 | 3.76 | 5.2 | 6.5187 | 7.77 | 9.0204 | 10.7183 | 12.0591 | 13.0427 | 13.7584 | 14.4742 | 15.1007 | 15.7272 | 16.2643 | 16.7122 | 17.0709 | 17.4295 | 17.7881 | 18.1467 | 18.4161 | 18.6854 | 18.9547 | 19.2241 | 19.4934 | 19.7628 | 19.9428 | 20.1229 | 20.3029 | 20.3937 | 20.4845 | 20.5752 | 20.666 | 20.6675 | 20.5797 | 20.4919 | 20.4041 | 20.3163 | 20.2285 | 20.1407 | 20.0529 | 19.9651 | 19.8773 | 19.7895 | 19.7017 | 19.6139 | 19.6153 | 19.5275 | 19.4397 | 19.4412 | 19.3534 | 19.3549 | 19.3564 | 19.3579
Mod Hyp: 4.8 m | 0 | 0.4 | 0.8 | 1.2 | 1.6 | 2 | 2.4 | 2.8 | 3.2 | 3.6 | 4 | 4.4 | 4.8 | 5.2 | 5.6 | 6 | 6.4 | 6.8 | 7.2 | 7.6 | 8 | 8.4 | 8.8 | 9.2 | 9.6 | 10 | 10.4 | 10.8 | 11.2 | 11.6 | 12 | 12.4 | 12.8 | 13.2 | 13.6 | 14 | 14.4 | 14.8 | 15.2 | 15.6 | 16 | 16.4 | 16.8 | 17.2 | 17.6 | 18 | 18.1 | 18.2 | 18.3 | 18.4 | 18.5
t = G ∙ gs
G/Gmax = 1 - (t/tmax)0.25
tmax = su = ½sinf'OCRLsvo'
OCR = 0.33(qt-svo)/svo'
Gmax = rt Vs2

## Slide 96
CREC Site, Charleston, SC (Esposito, Andrus & Camp 2014)
Frozen Sand Samples Taken
Clean
Sand (SP
and SP-SM)
Sand with
clay & shells
(SP-SC)
silty
Sand
(SM)
(marl)

## Slide 97: CREC Site, Charleston, SC Sand sampled using freezing (Esposito & Andrus 2016 JGGE)
SCPTu
SCPTu

## Slide 98: SCPTu in Memphis, Tennessee

## Slide 99: Input Parameters for Plaxis FEM (Schweiger 2012): Hardening Soil Small Model
Input from SCPTu
√ SBT or fs
√ Vs or fs
√ qt1
√ NTH Nm
√ qt1
n' = 0.2; nu = 0.5
√ Vs and Qtn
√ Ic and Qtn
√ Vs and Qtn
√ Ic
satm = 100 kPa
√ qt, OCR, f'
-
-
√ Vs
-

## Slide 100
Porewater Pressure Dissipation Tests
MONOTONIC
DILATORY

## Slide 101: SCPTù at Atlanta Airport Runway 5
Five Independent Readings of
Soil Behavior: qt, fs, u2, t50, Vs

## Slide 102
Standard rate of 20mm/s
Centrifuge CPTu Twitch Testing in Kaolin (Schneider 2007)
Notes: Check V

## Slide 103
Standard rate of 20mm/s
Centrifuge CPTu Twitch Testing in Kaolin (Schneider 2007)
Notes: Check V

## Slide 104: Variable Rate CPTu in Clay Centrifuge Deposit (Variable rate CPTu data from Mahmoodzadeh and Randolph 2014: University of Western Australia)
Notes: M&R

## Slide 105: Variable Rate CPTu in Clay Centrifuge Deposit (data from Mahmoodzadeh & Randolph 2014)
Lab Triaxial Tests
on Speswhite
Kaolin: f' = 21.6°
Notes: M&R

## Slide 106: Axial Pile Capacity: Qtotal = Qsides + Qbase
Qt
Shaft Capacity
Qs = ∫ fp dAs
Base Capacity
Qb = qb ∙ Ab
unit side
friction, fp
unit base resistance, qb
Atlanta Hartsfield
Vietnam Port Facility
Ground Surface

## Slide 107: Direct CPT Methods for Axial Pile Capacity
Aoki & de Alencar (1975 Pan-Am)
Schmertmann (1978, FHWA Rept)
de Ruiter & Beringer (1979)
Bustamante & Gianeselli (1982)
Zhou et al. (1982, ESOPT)
Tumay & Fakhroo (1982)
Price & Wardle (1982, ESOPT)
Van Impe (1986, 4th IGS)
Robertson et al. (1988, ISOPT-1)
Alsamman (1995, PhD, UIUC)
NGI-05 Clausen et al. 2005
Fioravante et al. (1995, 10th ARC)
Schneider et al. (JGGE 2008)
Lehane et al. (UWA 2012)
Niazi & Mayne (2015, 2017)
Almeida et al. (1996, BRE-NGI)
Eslami and Fellenius (1997)
Jardine & Chow (1996, MTD)
Takesue et al. (1998, KTRI)
Lee & Salgado (1999, ASCE JGGE)
Powell, et al. (2001, 15th ICSMGE)
Jamiolkowski (2003 BAP - Ghent)
Fugro-05 Kolk et al. 2005
ICP-05 Jardine et al. 2005
Abu-Farsakh & Titi (2004, JGGE)
UWA-05 Lehane et al. 2005
Xu et al. (2006, JGGE)
Van Dijk and Kolk (2011, ISFOG-II)

## Slide 108
www.mapcruzin.com
North America (40 Sites)
Canada: 11 Sites
USA: 28 Sites
Puerto Rico: 1 Site
Overview
330 pile load tests
70 sites
19 countries
China: 2
Iraq: 1
Japan: 2
Malaysia: 1
Thailand: 1
Asia (7 Sites)
Enhanced Unicone Method (Niazi & Mayne 2016)
Europe (21 Sites)
Belgium: 2
France: 4
Ireland: 3
Netherlands: 2
Norway: 2
Portugal: 1
United Kingdom: 7
CPT Soundings
SCPT/SCPTu: 59
CPTu: 9
CPT: 4
Unicone Method (1997): 102 load tests
Enhanced Unicone (2016): 330 load tests

## Slide 109
Cse = Cse(mean) ∙ qPileType ∙ qt-c ∙ qrate
Enhanced Unicone: Pile Side Friction: fp = Cse·qE
Compression: qt-c = 1.11
Tension/Uplift: qt-c = 0.85
Bored Piles: qPileType = 0.84
Jacked Piles: qPileType = 1.02
Driven Piles: qPileType = 1.13
Pile Type:
CRP: qrate = 1.09
MLT: qrate = 0.97
Direction of Loading:
Rate of Loading:
CRP = constant rate
of penetration
MLT = maintained load test
SIDE FRICTION
Pile End Bearing Resistance: qb = Cte·qE

## Slide 110
V
Qsu = S (fp dAs)
Qtu = Qs + Qb
Qbu = qb Ab
qE = qt - u2
Ic = fctn (Q and F)
RIGID PILE RESPONSE
Direct CPT Approach
qb = unit end bearing
unit side friction, fp
CPT
qt
u2
fs
Emax = 2 rt Vs2 (1+n)
Top Displacement, wt
Load Transfer
PILE
Vs
fp = fctn (Ic and qE)
qb = fctn (Ic and qE)

## Slide 111: I-85 Bridge, Coweta County, Georgia
Drilled Shaft Load Test: d = 0.914 m; L = 20.1 m

## Slide 112: SCPTu at I-85 Bridge Coweta Georgia

## Slide 113: Axial Load Response of Coweta Shaft
Qt
Qs
Qb

## Slide 114: GT Roto AutoSeis
Electro-Mechanical off 12-volt
AC or DC power; variable speed
Repeatable, Portable, reach 30-m depths
Can generate shear wavelets every 1 second
Patent received in February 2010

## Slide 115: Continuous Shear Waves, Brisbane, Australia

## Slide 116: Wavelet signals from continuous Vs at Norfolk
20 meter depth

## Slide 117: Continuous SCPTu at Norfolk, VA

## Slide 118: Very deep SCPTu - Vancouver, BC
460 feet =

## Slide 119: Thanks to the Cornell Professors
Fred H. Kulhawy
Dwight Sangrey
J. Neil Kay
Harry Stewart
Tom O'Rourke
Ken Hover
Lynne Irwin
John Abel
Peter Gergely
Dan Karig
Tony Ingraffea
Daniel P. Loucks
Yervant Terzian
Carl Sagan
Prof. Sherif
Wissa Agaiby
(1962-2019)
Prof. Fred
H. Kulhawy
(1943-2015)
Prof. Paul
W. Mayne -
Georgia Tech
Prof. Kok Kwang Phoon -
National
Univ. Singapore

## Slide 121: SCPTu Sounding in Albany, NY
Cone Resistance Sleeve Friction Porewater Pressure Shear Wave Velocity
qt (tsf) fs (tsf) u2 (feet) Vs (feet/sec)
Depth (feet)

## Slide 122: CPTu Databases from Chamber, Centrifuge and Field Tests
Bq=
Notes: Add Bq

## Slide 123: SCPTu from Steele, Missouri