## Slide 1: Stress History of Soils from Cone Penetration Tests
Paul W. Mayne, PhD, P.E.
Georgia Institute of Technology
Lisbon, 11 October 2017
34th Lição Manuel Rocha
Portuguese Geotechnical Society

## Slide 2: Manuel Rocha (1913-1981)
Victor de Mello (1985)
Nick Barton (1987)
Nordie Morgenstern (1989)
Mike Jamiolkowski(1997)
Mark Randolph (2000)
John Burland (2011)
Antonio Gomes Correira (2016)
Kerry Rowe (2006)
William Van Impe (2004)
Manuel Rocha
Lectures
Manuel Matos Fernandez (2009)
Eduardo Alonso (2013)

## Slide 3
Chart: Clays Sample from Evergreen, North Carolina
| 9.5749999999999996E-5 | 1.532 | 2.9682499999999998 | 6.0322500000000003 | 11.96875 | 23.9375 | 47.875 | 95.75 | 191.5 | 95.75 | 47.875 | 23.9375 | 47.875 | 95.75 | 191.5 | 383 | 766 | 1532 | 383 | 0.95750000000000002
 | 1.9074 | 1.898 | 1.8922 | 1.8797 | 1.8591 | 1.8088 | 1.7111 | 1.5663 | 1.3962 | 1.4076 | 1.4271 | 1.4445 | 1.4398 | 1.4271 | 1.3657 | 1.1762 | 0.95229 | 0.75691 | 0.81099 | 1.1087
svo' = 43 kPa
sp' = 80 kPa
(most probable)
Benchmark: Yield Stress from Consolidation Tests
Casagrande Method (1936)

## Slide 4: Effective Yield Stress or Preconsolidation Stress
Maximum past pressure, Pc’ = svmax’
Preconsolidation Stress, sp’
Apparent or quasi-preconsolidation
Yield Stress, svy’ (Leroueil 2003; Jardine 2003)
NORMALIZED FORMS
Overconsolidation Ratio: OCR = sp’/ svo’
Yield Stress Ratio: YSR = svy’/ svo’
Virtual OCR: vOCR (Viana da Fonseca 2014)
Complement to Lab Testing, Use of CPT and CPTu for Profiling sp’
= ROC

## Slide 5: Importance of Yield Stress and YSR = sp’/svo’
Separates NC and OC states
Settlement computations
Undrained strength: su/svo’ = ½·sinf’·YSRL
Geostatic stress state: K0 = (1-sinf’)·YSR sinf’
Porewater pressure behavior, Af
Anchors yield surface for constitutive soil models
Affects elastic modulus: E’ and Eu
Small-strain stiffness: Gmax = F(e)·p’·OCRk
Demarcates: contractive versus dilative behavior
Alternate to state parameter (y) for screening:
  flow liquefaction
  cyclic liquefaction
Soil
Mechanics
Soil
Dynamics

## Slide 6: Cavity Expansion-Critical State Model for CPTu-OCR
Clay Properties:
M = 6 sinf’/(3-sinf’)
f’ = effective friction angle
Cc = compression index
Cs = swelling index
L = 1 – Cs/Cc
IR = G/su = Rigidity Index
G = shear modulus
su = undrained shear strength
f’, Cc, Cs
Mayne (1991)
Chen & Mayne (1994)
Burns & Mayne (2002)
Mayne (2005, 2007)

## Slide 7: SCE-CSSM Analytical Solution
Notes:
M = 6 sinf'/(3-sinf')
IR = G/su
L = 1 – Cs/Cc ≈ 0.80
(clays and sands)
qt
u2
Clays

## Slide 8
qt
u2
fs
THIS U2

## Slide 9
Chart: Cone Tip Resistance qt (kPa)
Chart: Sleeve Friction fs (kPa)
Chart: Porewater Pressure u2 (kPa)
Chart: Shear Wave Velocity VS (kPa)
| 152 | 159 | 185 | 146 | 165 | 172 | 185 | 235
u2 | 4.5718 | 7.6196 | 10.6675 | 13.7153 | 16.7632 | 19.811 | 22.8589 | 25.9067
Sand
Brown
Clay
Seismic Piezocone Tests - Hartford, Connecticut
qt
u2
fs
Vs

## Slide 10
Chart: p' = 0.5 (s1' + s3') kPa
| 0 | 600
Strength Envelope | 0 | 234.4223
CIDC-1 | 0.33301 | 7.1506 | 13.9743 | 21.1733 | 26.8587 | 33.3009 | 38.9802 | 45.4285
CIDC-2 | 0.26641 | 10.8743 | 20.3499 | 29.4501 | 38.9257 | 46.1308 | 52.1916 | 58.6399 | 64.3253 | 67.7341 | 73.038 | 79.8677 | 85.1777
CIDC-3 | 0.24219 | 7.0598 | 17.2983 | 21.0825 | 27.5247 | 33.5855 | 40.0277 | 46.8514 | 53.669 | 58.2161 | 63.9014 | 70.719 | 75.2661 | 79.8132 | 86.2554 | 92.6976 | 98.0016 | 105.2006 | 109.7538 | 121.5181
CIDC-4 | 0.55703 | 5.1041 | 11.5463 | 16.0934 | 21.022 | 28.221 | 32.7742 | 38.0781 | 45.6586 | 51.7254 | 59.3059 | 64.6098 | 73.704 | 78.6325 | 83.5611 | 88.1082 | 94.5504 | 102.1309 | 108.1977 | 114.6399 | 118.4302 | 124.1155 | 130.9392 | 138.8951 | 143.8236 | 151.0227 | 155.5758
CIUC-1 | 0.59673 | 10.1262 | 19.6556 | 31.5902 | 42.3496 | 51.952 | 59.1675 | 66.4194 | 74.8831 | 79.8029 | 84.7591 | 86.0802 | 86.2444 | 86.3356 | 85.2516
CIUC-2 | 0.92246 | 6.8715 | 17.5762 | 31.8612 | 43.814 | 55.8034 | 64.2305 | 72.6942 | 80.0191 | 84.9389 | 89.8769 | 96.0996 | 101.0923 | 102.4134 | 106.1945 | 108.782 | 111.3696 | 112.709 | 112.782 | 112.8367 | 112.9096
f' = 23°
c' = 0
Brown Clay – Connecticut River, Hartford CT
Brown
Clay
Triaxial Test Results for Bissell Bridge

## Slide 11: Rigidity Index, IR – Hartford Connecticut
Krage, Broussard, & DeJong (CPT’14):
Chart: Rigidity Index, IR = G/su
| 108.82083733252087 | 139.18699924921779 | 126.61473742924959 | 137.59647556540986 | 224.24839549138792
Gmax qnet svo' | 13.75 | 16.75 | 19.85 | 22.85 | 25.45
Sand
Brown
Clay
IR = 128
G0 = rt ·Vs2
(consistent
units)

## Slide 12
Chart: YSR = Yield Stress Ratio
| 3.338855775669245 | 2.9422576464367967 | 2.8193647017101466 | 3.7955272681946792 | 3.1130635200599737 | 2.7489300432318711 | 2.3200582790403761
Consols | 10.6675 | 11.277 | 13.7153 | 14.0201 | 14.3249 | 23.1637 | 21.6397
Chart: Yield Stress, sp' (kPa)
Consols | 10.6675 | 11.277 | 13.7153 | 14.0201 | 14.3249 | 23.1637 | 21.6397
svo'
Sand
Firm
Brown
Clay
Hartford Connecticut

## Slide 13: SCE-CSSM Theory
For L = 1
f’ = 30o
IR = 100
First-Order Approximations

## Slide 14
Chart: CPTU Readings (MPa)
Soft Clay at Torp, Sweden (Larsson and Ånhberg 2006: SGI Report R-61)
Chart: Yield Stress, sp' (kPa)
Lab Consols | 4.0802 | 5.0505 | 6.0208 | 7.1297 | 8.1 | 8.9317 | 10.0406 | 11.0109 | 11.9812 | 12.9515 | 15.1693 | 16.001 | 16.8327 | 18.0802 | 19.0505 | 20.0208 | 22.1 | 24.0406 | 26.1198 | 26.9515 | 27.9218 | 30.001 | 32.0802 | 34.0208 | 35.9614 | 38.1792 | 39.9812 | 42.0604 | 44.001 | 44.9713 | 45.9416 | 47.0505 | 47.8822 | 48.9911 | 50.9317 | 53.0109 | 55.0901 | 57.0307
svo' | 0 | 4.0802 | 5.0505 | 6.0208 | 7.1297 | 8.1 | 8.9317 | 10.0406 | 11.0109 | 11.9812 | 12.9515 | 15.1693 | 16.001 | 16.8327 | 18.0802 | 19.0505 | 20.0208 | 22.1 | 24.0406 | 26.1198 | 26.9515 | 27.9218 | 30.001 | 32.0802 | 34.0208 | 35.9614 | 38.1792 | 39.9812 | 42.0604 | 44.001 | 44.9713 | 45.9416 | 47.0505 | 47.8822 | 48.9911 | 50.9317 | 53.0109 | 55.0901 | 57.0307
Chart: Yield Stress Ratio, YSR
Lab Consols | 4.0802 | 5.0505 | 6.0208 | 7.1297 | 8.1 | 8.9317 | 10.0406 | 11.0109 | 11.9812 | 12.9515 | 15.1693 | 16.001 | 16.8327 | 18.0802 | 19.0505 | 20.0208 | 22.1 | 24.0406 | 26.1198 | 26.9515 | 27.9218 | 30.001 | 32.0802 | 34.0208 | 35.9614 | 38.1792 | 39.9812 | 42.0604 | 44.001 | 44.9713 | 45.9416 | 47.0505 | 47.8822 | 48.9911 | 50.9317 | 53.0109 | 55.0901 | 57.0307
qt
u2
svo'
Soft
Clay

## Slide 15
Bothkennar Soft Clay, UK
(Hight et al. 2003)

## Slide 16
Port of Brisbane Expansion
Hydraulic sand fill over soft clay

## Slide 17
CPTu at Port of Brisbane
SOFT
CLAY
Hydraulic
Sand Fill

## Slide 18
Port of Brisbane

## Slide 19: Troll East, North Sea
(Uzielli et al. 2007; Lunne et al. 2007)
The Bucentaur (Courtesy: Fugro Engineers)

## Slide 20
Troll East, North Sea (Uzielli et al. 2007)

## Slide 21
Troll East, North Sea (Uzielli et al. 2007)

## Slide 22: Port of Anchorage, Alaska

## Slide 23: Anchorage Piezocone Sounding
qt
ub
fs

## Slide 24: Yield Stress Profile - Port of Anchorage
YSR = 5
YSR = 2

## Slide 25
by Jeff Keane

## Slide 26: Evaluating Yield Stresses in Sands by CPT
Oxford
University
Flexible Wall Chambers
Essentially large triaxial test
Four boundary conditions:
  BC1 – constant sv’ and constant sh’
  BC2 - Dev = 0 and Deh = 0
  BC3 – constant sv’ and Deh = 0
  BC4 – Dev = 0 and constant sh’
Virginia Tech
Calibration Chambers

## Slide 27: Calibration Chamber Testing
Mineralogy
Grain Distribution
Angularity
Index Parameters
Age
Origin
Dry or Saturated
Stress History
shc'
svc'
DR
eo
gT
qc
fs
u2
Artificial Sand
Deposit
BC1, BC2, BC3
BC4, and BC5
INVERSE PROBLEM

## Slide 28: CPT Chamber Test Series on Sands
Earlston
Edgar
Erksak
Frankston
Hilton Mines
Hokksund
Hostun
Lanchester
Leighton Buzzard
Light Castle Sand
Oosterschelde
Lone Star
Monterey
Ottawa
Reid-Bedford
South Oakleigh
Ticino
Toyoura
Washed Mortar Sand

## Slide 29
Chart: 1.973 (qnet)-0.828(svc')0.767(Ko)1.62
1.2 < OCR < 4 | 0.020027 | 0.022332 | 0.021801 | 0.012395 | 0.012902 | 0.021163 | 0.0058664 | 0.025085 | 0.062239 | 0.034588 | 0.008512 | 0.0090064 | 0.03925 | 0.020736 | 0.019794 | 0.0070387 | 0.017158 | 0.010005 | 0.012127 | 0.013214 | 0.012775 | 0.0085325 | 0.01467 | 0.039188 | 0.014503 | 0.0086842 | 0.021242 | 0.019788 | 0.024715 | 0.034338 | 0.051627 | 0.050173 | 0.035602 | 0.037018 | 0.02407 | 0.0091357 | 0.010226 | 0.0093655 | 0.0088807 | 0.008842 | 0.0091606 | 0.013781 | 0.029626 | 0.013126 | 0.0098815 | 0.039523 | 0.0087814 | 0.012342 | 0.054981 | 0.031789
4.1 < OCR < 6 | 0.020027 | 0.022332 | 0.021801 | 0.012395 | 0.012902 | 0.021163 | 0.0058664 | 0.025085 | 0.062239 | 0.034588 | 0.008512 | 0.0090064 | 0.03925 | 0.020736 | 0.019794 | 0.0070387 | 0.017158 | 0.010005 | 0.012127 | 0.013214 | 0.012775 | 0.0085325 | 0.01467 | 0.039188 | 0.014503 | 0.0086842 | 0.021242 | 0.019788 | 0.024715 | 0.034338 | 0.051627 | 0.050173 | 0.035602 | 0.037018 | 0.02407 | 0.0091357 | 0.010226 | 0.0093655 | 0.0088807 | 0.008842 | 0.0091606 | 0.013781 | 0.029626 | 0.013126 | 0.0098815 | 0.039523 | 0.0087814 | 0.012342 | 0.054981 | 0.031789
10 < OCR < 15 | 0.034871 | 0.022373 | 0.034602 | 0.033017 | 0.021623 | 0.0321 | 0.035956 | 0.027692 | 0.031552 | 0.022171 | 0.028969 | 0.031364 | 0.036955 | 0.030086 | 0.029397 | 0.024813 | 0.032102 | 0.032153 | 0.046243 | 0.047679
26 Different Sands
n = 626
CPT Chamber Test Data on Sands

## Slide 30: CPT Methodology for Ko and OCR in sands
Regression from CPT Calibration Chamber Database (n = 705 data points; r2 = 0.871): Ko = 0.192(qt/satm)0.22 (svo’/satm)-0.31 YSR 0.27
Relationship between Ko and OCR a priori: Ko = (1-sinf’) YSR sin f’
Evaluate Effective Stress Friction Angle from Kulhawy & Mayne (1990): f’ = 17.6°+11log(qt1)
where: qt1 = (qt/satm)/(svo'/satm)0.5

## Slide 31
Rhymes with Orange
by Hilary Price "THE LAB"

## Slide 32: CPT Methodology in Clean Quartz Sands
Apparent Overconsolidation Ratio, OCR (or Yield Stress Ratio, YSR):
f’ = effective stress friction angle
qt = cone tip resistance
svo’ = effective vertical stress
satm = atmospheric pressure (1 bar = 100 kPa)

## Slide 33: CPT Methodology in Clean Quartz Sands
Yield Stress Ratio, YSR (or vOCR):
Assume characteristic value: f’ = 35
Sands: qt ≈ (qt - svo)
Simplified:
Preconsolidation Stress:

## Slide 34: CPT methodology for all soil types
Reduction of SCE-CSSM model for CPTu in clay:
Simplification of regression equations from CPT calibration chamber tests data on clean sands:
General form:
Exponent m' varies: clay m' = 1.0; sand m' = 0.72

## Slide 35: Effective Yield Stress of Soils from CPT
Chart: Net Cone Resistance, qt - svo (kPa)
| 1 | 100000
Trend - Intact Clays | 0.33 | 33000
Trend - Silts | 0.33 | 5868.3221
Trend - Clean Sands | 0.33 | 1313.7537
Opelika Sandy Silt | 210 | 216.72 | 230.86 | 266.56 | 273
Stockholm Sand | 280 | 294 | 312 | 327 | 347 | 361 | 377 | 393
Vagverket Silt | 77.175 | 92.61 | 108.045 | 123.48 | 138.915 | 154.35 | 169.785 | 185.22 | 200.655 | 216.09
Po River Sand | 194.23 | 202.52 | 210.81 | 219.1 | 227.39 | 235.68 | 243.97 | 268.84 | 285.42 | 302
Sensitive Clays - Organics | 0.33 | 10435.5163
Pentre Silt | 177.1028 | 222.8022 | 268.5015 | 322.2183 | 359.0985 | 406.4013
Holmen Sand | 43.884 | 59.94 | 75.996 | 92.052 | 108.108 | 124.164 | 140.22 | 156.276 | 172.332
CLAYS
SILTS / MIXED
SANDS
sp' =0.33(qtnet)m

## Slide 36: 9-Zone Soil Behavioral Type Charts for CPT (Robertson 1990, 1991)
1. Normalized Tip Resistance: Q = (qt - svo)/svo'
2. Normalized Sleeve Friction (%): F = 100  fs/(qt - svo)
3. Normalized Porewater Pressure: Bq = (u2-u0)/(qt - svo)

## Slide 37: Soil Behavioral Type by CPT
CPT Material Index (Ic) for identification of soil type (Robertson & Wride, 1998):
Modified normalized tip resistance (Robertson 2004):
Exponent n = 0.5 (sands), 0.75 (silts), n = 1.0 (clays)
Iterate to find exponent n (Robertson 2009 CGJ):
sands: Ic < 2.05
clays: Ic > 2.95

## Slide 38
Soil Behavioral
Type (SBTn) Chart
for normalized CPT
(after Robertson 2009)
a. Find sensitive soils of zone 1 identified when: Qtn < 12 exp(-1.4 Fr )
b. Identify: Zone 8 (1.5 < Fr< 4.5%) and Zone 9 (Fr > 4.5%):
c. Use CPT index Ic for Zones 2 through 7
Approximate
Algorithm Steps:
Ic < 2.6: Drained
Ic > 2.6: Undrained

## Slide 39: Burswood clay test site, Perth, Australia

## Slide 40: Preconsolidation Stress from CPT qnet and Ic
Burswood Clay, Perth, Australia
sp' = 0.33(qtnet)
Soft
Alluvial
Clay

## Slide 41: National Geotechnical Experimentation Site Piedmont Residual fine sandy Silts, Opelika, Alabama

## Slide 42: Preconsolidation Stress from CPT qnet and Ic
National Test Site, Opelika, Alabama:
sp' = 0.33(qtnet)0.85
Residual
Silts and
Sands

## Slide 43: Blessington Sand Site University of College Dublin (UCD)
Doherty et al. (2012)
Tolooiyan & Gavin (2011)

## Slide 44
Chart: Cone Resistance, qt (MPa)
Chart: Yield Stress Ratio, YSR
Consolidation Tests | 2.8696 | 1.7609 | 1.8261 | 1.7609 | 2.8696 | 5.6087 | 6.587 | 10.0435 | 9.9783 | 11.8696 | 13.8913 | 13.8913 | 11.9348
Consolidation
Tests
Dense
Fine
Sand
Dense OC Sand Site, Blessington, Ireland
(Dougherty et al. 2012; Gavin et al. 2014)

## Slide 45
Unified Approach: Yield Stress versus Net Cone Resistance

## Slide 46
Chart: Gravelly Sands Sandy Silty Clays Organic Sand Mix Mix
Hibernia Sand | 0.7
Euripides Sand | 0.78
Holmen Sand | 0.73
Po River Sand | 0.72
Blessington Sand | 0.74
Piedmont SM | 0.8
Piedmont ML | 0.83
Pentre Silt | 1
Vagverket Silt | 0.75
Mjardevi Silt | 0.8
Os Silt, Norway | 0.95
Fissured
Clays
Intact Clays
Silts
Quartz and
Silica Sands
CLAYS
SILTS
SANDS
For Ic < 3.5
Yield Stress Exponent m’ Trend with CPT Material Index, Ic
Zone No. = 7 6 5 4 3 2

## Slide 47
Golden Ears Bridge, British Columbia, Canada
Amini et al. (2008), Niazi et al. (2010)

## Slide 48: Golden Ears Bridge, British Columbia (Niazi et al. 2012)
Chart: Cone Tip Resistance
Chart: Sleeve Friction
Chart: Porewater Pressure
Chart: Shear Wave Velocity
Sensitive
CLAY
CLAY
SAND
SILT
m’ = 0.85
m’ = 0.72
m’ = 1.0
m’ = 1.0
Soft and
Loose
Holocene
Deposits

## Slide 49
Chart: CPT Material Index, IC
Gr Sand | 0 | 140
Sand | 0 | 140
Sand Mix | 0 | 140
Silt | 0 | 140
Clay | 0 | 140
Gravelly Sand
Sand
Sand Mix
Silt Mix
Clay
Organic
Chart: SBT Zone
Chart: Effective Stress (kPa)
SILT
SAND
CLAY
Sensitive
CLAY
Golden Ears Bridge, British Columbia (Niazi et al. 2010)
CPT Interpretation of Yield Stress in Layered Soils
svo’
sp’=0.33qnetm’
m’ = 0.85
m’ = 0.72
m’ = 1.0
m’ = 1.0

## Slide 50
Chart: CPT Material Index, IC
Gr Sand | 0 | 140
Sand | 0 | 140
Sand Mix | 0 | 140
Silt | 0 | 140
Clay | 0 | 140
Gravelly Sand
Sand
Sand Mix
Silt Mix
Clay
Organic
Chart: SBT Zone
Chart: Effective Stress (kPa)
SILT
SAND
CLAY
Sensitive
CLAY
Golden Ears Bridge, British Columbia (Niazi et al. 2010)
CPT Interpretation of Yield Stress in Layered Soils

## Slide 51: CPT sp’ Method Applicable to “Hourglass Sands” and “Vanilla” Clays
Quartz-Silica Sands Inorganic Clays
Uncemented of low sensitivity

## Slide 52: What about “Chocolate” Clays ?
Milk Chocolate Clay
Dark
Chocolate Gelato Clay with
Hazelnuts

## Slide 53: Profiling Yield Stress in Clays by CPT
0.43
0.33
0.16

## Slide 54
Chart: Cone Tip Resistance qt (kPa)
Chart: Sleeve Friction fs (kPa)
Chart: Porewater Pressure u2 (kPa)
Piezocone CPTU-L2 in Mexico City Clay
(Cruz and Mayne, GeoShanghai 2006)

## Slide 55
Chart: YSR = Yield Stress Ratio
Consols | 7.5145 | 12.7168 | 20.6936 | 36.763
Stress History from CPTu in Mexico City Clay
(Cruz and Mayne, GeoShanghai 2006)
Simplified Solution DOES NOT WORK
Chart: Yield Stress, sp' (kPa)
Consols | 7.5145 | 12.7168 | 20.6936 | 36.763
svo' | 1
WARNING
SIGN

## Slide 56
Mesri (1975, Geotechnique):
Zeevaert (1957):
Mexico City Clay

## Slide 57
Piezocone CPTu-L2 in Mexico City Clay
(Robertson 1991, 2009)

## Slide 58
Unified Approach: Yield Stress versus Net Cone Resistance

## Slide 59
Chart: Yield Stress, sp' (kPa)
Consols | 7.5145 | 12.7168 | 20.6936 | 36.763
Chart: YSR = Yield Stress Ratio
Consols | 7.5145 | 12.7168 | 20.6936 | 36.763
Stress History from CPTu in Mexico City Clay
(Cruz and Mayne, GeoShanghai 2006)
Organic Clays: sp’ (kPa) = 0.33 (qt – svo)0.90

## Slide 60
Sarapui II soft organic clay, Brazil (Jannuzzi et al. 2016)
Consols
sp’ = 0.33 qnet0.88
Yield Stress: sp’ = 0.33 qnet0.88

## Slide 61
"You need a new recipe. This mud tastes terrible"

## Slide 62
Evaluate Flow Liquefaction Potential by CPT
Rather Involved and Complex Relationships
Correction for Fines Content adds Uncertainty
Simple Procedure
1. State Parameter for Sands from CPT (Been et al 1987, Jefferies & Been 2005)
2. Equivalent normalized cone resistance for clean sands, Qtn-cs = Kc·Qtn (Robertson 2010)
3. CPT evaluation of yield stress ratio at critical state line: YSRCSL ≈ 3

## Slide 63
Logarithm Effective Stress, sv'
Void Ratio, e
VCL
CSL
e0
eCSL
Dilative:
y = e0 - eCSL < 0
Define: State Parameter
y = e0 - eCSL
(e0, P0')
Virgin compression line
Critical state line
e0
Contractive:
y = e0 - eCSL > 0
(e0, P0')

## Slide 64: State Parameter for Sands from CPT (Been et al 1987, Jefferies & Been 2005, 2016)
1/l10
1/l10 = 34 - 10·Ic-JB
CPT Material Index, Ic-JB
l10 = slope of e-log10(p’)

## Slide 65: State Parameter for Sands from CPT (Been et al 1987, Jefferies & Been 2005, 2016)
Qp = (qt – p)/p’
State Parameter, y

## Slide 66: Modified State Parameter for Tailings from CPT (Been et al 2012, Jefferies & Been 2016)
1/l10 = 34 - 10·Ic-JB
CPT Analyses
Lab Testing
M = 6·sinf’/(3-sinf’)

## Slide 67
Chart: CPT Soil Behavioral Type Chart
Zone 9 | 85 | 200 | 300 | 400 | 500 | 600 | 800 | 1000 | 1200
Gravelly SANDS
(Zone 7)
SANDS
(Zone 6)
Sandy Mix
(Zone 5)
Silty Mix
(Zone 4)
CLAYS
(Zone 3)
Organic
(Zone 2)
Sensitive Soils
(Zone 1)
Stiff
clayey
Sand
(Zone 8)
Very
Stiff
clays
and
silts
(Zone 9)
Robertson (2012) Procedure for Flow Liquefaction

## Slide 68: Adjustment for Sand Fines Content
For Ic ≤ 1.64: Kc = 1.0
For Ic > 1.64: Kc = - 0.403 Ic4 + 5.581 Ic3 - 21.63 Ic2 + 33.75 Ic - 17.88
Equivalent Normalized Cone Resistance: Qtn-cs = Kc · Qtn
For clean sands

## Slide 69: CPT SBT Liquefaction Susceptibility
A1 = Sands: Cyclic Liquefaction Possible
A2 = Sandy to Silty Soils: Cyclic and Flow Liquefaction Possible
B = Clays and Silts: Cyclic softening Possible
C = Sensitive Clays: Flow Liquefaction and Cyclic Softening Possible
(Robertson 2010)
Regions

## Slide 70
(Robertson 2010, 2016)
Flow Liquefaction Susceptibility
Contractive Soils are susceptible to flow liquefaction
Theoretically contractive when y > 0
Practical threshold when y > -0.05
Estimate y = 0.485 - 0.314·log(Qtn-cs)
Contractive when Qtn-cs < 70
<

## Slide 71: Gold Tailings, Western USA (Been et al. 2012)
Chart: Cone Resistance, qt (MPa)
Chart: Sleeve Friction, fs (kPa)
Chart: Pore Pressure, u2 (kPa)
Loose
to Soft
Tailings

## Slide 72
Gold Tailings, Western USA (Been et al. 2012)
Chart: State Parameter, Y
Contractive-Dilative | 0 | 30
Chart: Normalized Qtn -cs
Qtn-cs = 70 | 0 | 30
Contractive Dilative
Chart: Cone Resistance, qt (MPa)
Jefferies
& Been
y = -0.05
Robertson
Qtn-cs = 70

## Slide 73
Logarithm Effective Stress, sv'
Void Ratio, e
VCL
CSL
e0
su = (sinf'/2)∙YSRL ∙ svo'
Du = (1 - ½ cos f' YSRL )∙ svo'
where L = 1 - Cs/Cc
Cc
svo'
sy'
Cs
Yield Stress
Effective
Overburden Stress
Yield Stress Ratio
= YSR = sy'/svo'
-Du
Normally Consolidated (NC)
Overconsolidated (OC)
Simplified Critical-State Soil Mechanics
+Du

## Slide 74
Logarithm Effective Stress, sv'
Void Ratio, e
Virgin Compression
Line, VCL
Critical State
Line, CSL
e0
Simplified Critical State Soil Mechanics
Cc
svo'
sp'
Cs
Yield Stress
Effective
Overburden
Stress
Yield Stress Ratio
= YSR = sp'/svo'
Normally Consolidated (NC)
Overconsolidated (OC)
y = - Cc ∙ log[ ½∙cos f'∙YSRL ]
L = 1 - Cs/Cc ≈ 0.8 (sands & clays)
State Parameter
= y = e0 - eCSL
eCSL
drained
undrained
su = (sinf'/2)∙YSRL ∙ svo'
Du = (1 - ½ cos f' YSRL )∙ svo'
Contractive
Behavior
Dilative
Behavior
YSRCSL = (2/cos f')1/L

## Slide 75
CPT Screening for Flow Liquefaction
1. State Parameter: y = e0 - eCSL > 0
2. Yield Stress Ratio: YSRCSL < (2/cos f')1/L
Soils are contractive when:
(or approximate threshold: YSRCSL < 3)
(practical threshold: y > - 0.05 )
(Robertson 2016: OCR < 4)

## Slide 76: Gold Tailings, Western USA (Been et al. 2012)
Chart: CPT Material Index, IC
Gr Sand | 0 | 35
Sand | 0 | 35
Sand Mix | 0 | 35
Silt Mix | 0 | 35
Clay | 0 | 35
Chart: SBTn Zone No.
Chart: Effective Stress (kPa)
svo'
Clay
Silts
Sandy Mixs
Sands
sp‘= 0.33qnetm’

## Slide 77
Gold Tailings, Western USA (Been et al. 2012)
Chart: YSR = Yield Stress Ratio
Chart: State Parameter, Y
Contractive-Dilative | 0 | 30
Chart: Resistance, Qtn -cs
Qtn-cs = 70 | 0 | 30
Contractive Dilative
Contractive Dilative
YSR at
critical state
= (2/cosf')1/L

## Slide 78
Flow Liquefaction Case Study
Sands Head, Fraser River Delta, BC (Christian et al., 1997 CGJ)

## Slide 79: Sands Head, Fraser River Delta, BC
Chart: Cone Resistance, qt (MPa)
Chart: Sleeve Friction, fs (kPa)
Chart: Pore Pressure, u2 (kPa)
(Christian et al. 1997)

## Slide 80: Sands Head, Fraser River Delta, BC
Chart: CPT Material Index, IC
Gr Sand | 0 | 35
Sand | 0 | 35
Sand Mix | 0 | 35
Silt Mix | 0 | 35
Clay | 0 | 35
Chart: YSR = Yield Stress Ratio
Chart: Resistance Qtn -cs
Limits | 0 | 30
YSR at
critical state
Qtn-cs = 70
Contractive Dilative

## Slide 81: Kingston Flyash Failure, Tennessee (22 Dec 2008)
Flow Liquefaction Case Study
TVA stockpile dam fails into Emory River

## Slide 82: Kingston Flyash Failure, Tennessee (Robertson 2010)
Chart: Cone Resistance, qt (MPa)
Chart: Sleeve Friction, fs (kPa)
Chart: Pore Pressure, u2 (kPa)
Flow Liquefaction Case Study
qt
u2
fs

## Slide 83
Chart: CPT Material Index, IC
Gr Sand | 0 | 35
Sand | 0 | 35
Sand Mix | 0 | 35
Silt Mix | 0 | 35
Clay | 0 | 35
Chart: YSR = Yield Stress Ratio
Chart: Resistance Qtn-cs
Qtn-cs = 70 | 0 | 18
Contractive Dilative
YSRCSL
Qtn-cs = 70
Kingston Flyash Failure, Tennessee (Robertson 2010)
Flow Liquefaction Case Study
Weak Layer
Weak Layer
Clay
Silt
Sandy Mix
Sand

## Slide 84: Neves Corvo Tailings, Portugal
Liquefaction potential of paste fill at Neves Corvo mine, Portugal
K. Been, E. T. Brown & N. Hepworth published online 05 Sept 2013

## Slide 85: CPT-001 Neves Corvo Tailings, Portugal Flow Liquefaction Screening Evaluation (Been et al 2002)
Chart: Cone Resistance qt (MPa)
Chart: CPT Material Index IC (R&W 1998)
Gr Sand | 0 | 35
Sand | 0 | 35
Sand Mix | 0 | 35
Silt Mix | 0 | 35
Clay | 0 | 35
Gravelly Sand
Sand
Sand Mix
Silt Mix
Clay
Organic
Chart: Yield Stress Ratio YSR = sp’/svo’
Chart: State Parameter Y (J&B 2006)
Contractive-Dilative | 0 | 30
Dilative Contractive
Been
et al
(2002)
Tailings
Underconsolidated
YSR < 1

## Slide 86: CPT Evaluation of Cyclic Soil Liquefaction
Haiti (2010) courtesy Glenn Rix
Haiti 2010 (courtesy Univ. Idaho)
Tohoku Japan 2011
Chile 2010 (courtesy J. Bray & J.D. Frost)

## Slide 87: Cyclic Liquefaction Evaluation by CPT
(Youd, et al. 2001; Boulanger & Idriss 2014)
Simplified Approach uses Cyclic Stress Ratio (CSR):
t = average cyclic shear stresses
amax/g = PGA = peak (horiz.) ground acceleration
svo = total vertical (overburden) stress
svo' = effective vertical stress
rd = stress reduction coefficient
MSF = magnitude scaling factor convert to Mw = 7.5

## Slide 88: Simplified Cyclic Stress-Based Procedures
Level of Ground Shaking:
Soil resistance based on in-situ field tests:
  SPT = standard penetration
  CPT = cone penetration
  Vs = shear wave velocity
  DMT = flat dilatometer
Compare CSR with Cyclic Resistance Ratio (CRR) for likelihood for liquefaction.
Chart: In-Situ Soil Resistance from SPT, CPT, DMT, or Vs
| 1 | 2 | 3 | 4 | 5 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180 | 185 | 190
Robertson & Wride 1998 | 0.05082 | 0.051653 | 0.052486 | 0.053319 | 0.054152 | 0.054984 | 0.05665 | 0.058316 | 0.059981 | 0.061647 | 0.063312 | 0.064978 | 0.066644 | 0.070808 | 0.074972 | 0.079136 | 0.083299 | 0.087463 | 0.091602 | 0.095449 | 0.10006 | 0.10551 | 0.11187 | 0.11921 | 0.12758 | 0.13708 | 0.14776 | 0.1597 | 0.17296 | 0.18761 | 0.20373 | 0.22139 | 0.24064 | 0.26158 | 0.28425 | 0.30874 | 0.33511 | 0.36343 | 0.39378 | 0.42622 | 0.46081 | 0.49765 | 0.53678 | 0.57828 | 0.62222 | 0.66868 | 0.71771
Liquefaction
Likely
Liquefaction
Not Likely
CRR

## Slide 89: Cyclic Liquefaction Evaluation by CPT
(Robertson & Wride 1998; Youd et al. 2001)
Evaluate the Cyclic Resistance Ratio (CRR) of clean sands from CPT stress-normalized cone resistance (Qtn)
For range: 50 ≤ Qtn ≤ 160
For Qtn < 50

## Slide 90: Evaluate Soil Liquefaction by CPT
Chart: Normalized Cone Resistance, (Qtn)
| 1 | 2 | 3 | 4 | 5 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180 | 185 | 190
CRR | 0.05082 | 0.051653 | 0.052486 | 0.053319 | 0.054152 | 0.054984 | 0.05665 | 0.058316 | 0.059981 | 0.061647 | 0.063312 | 0.064978 | 0.066644 | 0.070808 | 0.074972 | 0.079136 | 0.083299 | 0.087463 | 0.091602 | 0.095449 | 0.10006 | 0.10551 | 0.11187 | 0.11921 | 0.12758 | 0.13708 | 0.14776 | 0.1597 | 0.17296 | 0.18761 | 0.20373 | 0.22139 | 0.24064 | 0.26158 | 0.28425 | 0.30874 | 0.33511 | 0.36343 | 0.39378 | 0.42622 | 0.46081 | 0.49765 | 0.53678 | 0.57828 | 0.62222 | 0.66868 | 0.71771
for clean sands (Robertson & Wride 1998)
NCEER (2001)

## Slide 91: Cyclic Liquefaction Evaluation by CPT
Effect of Fines Content (FC) on CRR (Boulanger and Idriss 2014)

## Slide 92: Liquefaction Evaluation of Sands by CPT
Qtn = (qt - svo)/(svo')n (in units of bars or atmospheres)
NCEER/NSF
(Youd, et al.
2001)
Robertson & Wride (1998 CGJ);
Robertson
(2010, CGJ)
Exponent n ≈ 0.5 ± 0.2

## Slide 93: San Felipito Bridges Baja, Mexico PGA = 0.27 g
Epicenter
APRIL 4, 2010
M 7.2
EL MAYOR-CUCAPAH
EARTHQUAKE
Liquefaction Case Study (Turner et al. 2016) San Felipito Bridges, Baja, Mexico

## Slide 94: San Felipito Bridges, Mexico (Turner et al. 2014)
Highway Bridge on
On Drilled Shafts - Okay
Railroad Bridge on
Driven Pilings – Lost Segment

## Slide 95: San Felipito Bridge, Mexico
Sands
with
silty sandy
layers

## Slide 96: San Felipito Bridge, Mexico
Chart: Normalized Cone Resistance
Chart: CPT Material Index, IC (R&W)
Gr Sand | 0 | 35
Sand | 0 | 35
Sand Mix | 0 | 35
Silt Mix | 0 | 35
Clay | 0 | 35
Gravelly Sand
Sand
Sand Mix
Silt Mix
Clay
Organic
Chart: 

## Slide 97: San Felipito 2010 EQ (Turner et al 2014, 2016) M = 7.2; PGA = 0.27
Factor of Safety
FS = CRR7.5/CSR7.5

## Slide 98: San Felipito Liquefaction
Sandy Layers
Identified as
Contractive
FS = CRR7.5/CSR7.5

## Slide 99: Marina District, San Francisco CA (Loma Prieta EQ 1989) (Zhang, et al. CGJ 2002): M=7.0 and PGA = 0.20
Chart: Cone Resistance qt (MPa)
Chart: CPT Material Index, IC
Gr Sand | 0 | 35
Sand | 0 | 35
Sand Mix | 0 | 35
Silt Mix | 0 | 35
Clay | 0 | 35
Gravelly Sand
Sand
Sand Mix
Silt Mix
Clay
Organic
Chart: Yield Stress Ratio YSR
Chart: CRR and CSR
Critical
Layer 1
Critical
Layer 2
CSL
Threshold
YSR

## Slide 100: Moss Landing, CA: Mw=7.0; PGA = 0.25 g
Kulasingam, R., Boulanger, R. W., and Idriss, I. M. (1999).
Proceedings, 7th US-Japan Workshop on Earthquake Resistant Design of Lifeline Facilities and Countermeasures Against Liquefaction, Technical Report MCEER-99-0019, MCEER, SUNY, Buffalo, 35-54.
Chart: Cone Resistance, qt (MPa)
Chart: CPT Material Index, IC
Gr Sand | 0 | 35
Sand | 0 | 35
Sand Mix | 0 | 35
Silt Mix | 0 | 35
Clay | 0 | 35
Gravelly Sand
Sand
Sand Mix
Silt Mix
Clay
Organic
Chart: Yield Stress Ratio, YSR
CSL
Threshold
YSR
Chart: Calculated Factor of Safety, FS
Critical | 0 | 33
FS = CRR7.5/CSR7.5
Critical
Layer 1
Critical Layer 3
Critical Layer 2

## Slide 101: Cyclic Liquefaction – 4 EQs in NZ (2010-2011)
Christchurch NZ 2011
Christchurch NZ 2011
Christchurch (Green 2010)
Christchurch (Green 2010)

## Slide 102
Christchurch Site 11, North Kaiapoi, New Zealand
(CPT-KAN-26 from Green et al. 2014, Earthquake Spectra)
Critical
Layer 1
Critical
Layer 2

## Slide 103: Site 19, Brighton, Christchurch 2011 Earthquake Liquefaction Case (Green et al 2014)
Chart: Cone Resistance, qt (MPa)
Chart: CPT Material Index, IC
Gr Sand | 0 | 35
Sand | 0 | 35
Sand Mix | 0 | 35
Silt Mix | 0 | 35
Clay | 0 | 35
Gravelly Sand
Sand
Sand Mix
Silt Mix
Clay
Organic
Chart: Yield Stress Ratio, YSR
Chart: CRR7.5 and CSR7.5
Critical
Layer 1
Critical
Layer 2
Liquefied
Sand
M = 6.2 and PGA = 0.35

## Slide 104
Scale:
PGA = amax (m/s2)
Seismic Map of USA: New Madrid Seismic Zone
1811-1812: Mw = 7.1, 8.1, and 7.6
www.usgs.gov
Occurred about 56 years
After the 1755 earthquake
In Portugal

## Slide 105: Walker Paleoliquefaction Site, Marked Tree New Madrid Seismic Zone (Liao & Mayne 2010; Tuttle 1999): Mw = 7.6 and PGA = 0.19 g

## Slide 106: Marked Tree, Arkansas (NMSZ): GWT 2 to 5 m
Likely
Likely
Likely
Marginal
Overconsolidation Ratio CRR and CSR

## Slide 107: Lesson: Yield stress of soils from CPT
For intact inorganic clays:
sp’ = 0.33·(qt – svo)
sp’ = 0.53·(u2 – u0)
sp’ = 0.60·(qt – u2)
For uncemented quartz-silica sands
sp’ (kPa) = 0.33·(qt – svo)0.72
“Vanilla” Clay
“Hourglass” Sand
MATCH

## Slide 108: Lesson: Yield stress of soils from CPT
Yield Stress (kPa): sp’ = aq·(qt – svo)m’
aq = fctn( f’, IR = G/su, mineralogy)
For f’ = 30°, IR = 100, then aq = 0.33
sp’ (kPa) = 0.33·(qt – svo)m’
Exponent m’ = 1.1 Fissured Clays
1.0 Intact inorganic clays
0.9 Organic clays
0.85 Silts
0.80 Sandy Silts
0.75 Silty Sands
0.72 Clean quartz-silica sands
For quartz-silica sands and inorganic clays of low-medium sensitivity, m’ is related to CPT Material Index, Ic
Brazilian
Clays
Brazilian
Clays
aq = 0.15

## Slide 109
Chart: Gravelly Sands Sandy Silty Clays Organic Sand Mix Mix
Hibernia Sand | 0.7
Euripides Sand | 0.78
Holmen Sand | 0.73
Po River Sand | 0.72
Blessington Sand | 0.74
Piedmont SM | 0.8
Piedmont ML | 0.83
Pentre Silt | 1
Vagverket Silt | 0.75
Mjardevi Silt | 0.8
Os Silt, Norway | 0.95
Fissured
Clays
Intact Clays
Silts
Quartz and
Silica Sands
CLAYS
SILTS
SANDS
For Ic < 3.5
Yield Stress Exponent m’ Trend with CPT Material Index, Ic
Zone No. = 7 6 5 4 3 2

## Slide 110
Lesson: CPT Screening for Flow and Cyclic Liquefaction
1. State Parameter: y = e0 - eCSL > 0
2. Yield Stress Ratio: YSRCSL < (2/cos f')1/L
Soils are contractive when:
(or approximate threshold: YSRCSL < 3)
(practical threshold: y > - 0.05 )
Simpler and direct approach
Contractive soils are prone
to liquefaction; i.e. loose sands

## Slide 111
Obrigado